## Slide 1: A+ Guide to Managing & Maintaining Your PC, 8th Edition
Chapter 5
Supporting Processors and Upgrading Memory

## Slide 2: Objectives
Learn about the characteristics and purposes of Intel and AMD processors used for personal computers
Learn how to install and upgrade a processor
Learn about the different kinds of physical memory and how they work
Learn how to upgrade memory

## Slide 3: Types and Characteristics of Processors
Processor
  Installed on motherboard
  Determines system computing power
Two major processor manufacturers
  Intel and AMD
Figure 5-1 An AMD Athlon 64 X2 installed in socket AM2+ with cooler not yet installed

## Slide 4: Types and Characteristics of Processors
Features affecting processor performance and compatibility with motherboards
  Clock speed the processor supports
  Processor speed
  Socket and chipset the processor can use
  Processor architecture
  Multiprocessing abilities
    Dual processors
    Multi-core processing
    Multithreading

## Slide 5: Types and Characteristics of Processors
Features affecting processor performance and compatibility with motherboards (cont’d)
  Memory cache
  Memory features on the motherboard that the processor can support
  Support for virtualization
  Integrated graphics

## Slide 6: How a Processor Works
Basic components
  Input/output (I/O) unit
    Manages data and instructions entering and leaving the processor
  Control unit
    Manages all activities inside the processor
  One or more arithmetic logic units (ALUs)
    Performs all logical comparisons, calculations

## Slide 7: How a Processor Works
Basic components (cont’d)
  Registers
    Small holding areas on processor chip
    Holds counters, data, instructions, and addresses ALU is currently processing
  Internal memory caches (L1, L2, L3)
    Holds data and instructions to be processed by ALU
  Buses
    Connect components within the processor housing

## Slide 8
Figure 5-3 Since the Pentium processor was first released in 1993, the standard
has been for a processor to have two arithmetic logic units so that it can process
two instructions at once

## Slide 9: How a Processor Works
Processor frequency (speed)
  Speed at which processor operates internally
Multiplier
  Factor multiplied against system bus frequency
    Determines processor frequency
  System bus frequency × multiplier = processor frequency
Processor sold today contain ALUs and registers that can process 32 bits or 64 bits at a time

## Slide 10: How a Processor Works
Three categories of processors:
  32-bit processors – known as x86 processors
    Can handle 32-bit instructions from OS
  Hybrid processors – known as x86-64 processors
    Can handle a 32-bit OS or a 64-bit OS
    AMD produced the first one (called AMD64)
  64-bit processors – known as x64 processors
    Require a 64-bit OS and can handle 32-bit applications only by simulating 32-bit processing

## Slide 11: How a Processor Works
Memory cache (L1, L2, or L3)
  Each core in a processor has its own L1 and L2 caches
  All cores might share an L3 cache within the processor package
  Improves performance
Memory controller
  Included in processor package
  Significant increase in system performance

## Slide 12
Figure 5-4 Quad-core processing with L1, L2, and L3 cache and the memory controller within the processor housing

## Slide 13
Table 4-1 Current Intel processors

## Slide 14
Table 4-1 Current Intel processors (continued)

## Slide 15: Intel Processors
Processor identification
  Processor number
    Example: two Core i7 processors are identified as:
      i7-940 and i7-920
Centrino technology improves laptop performance
  Processor, chipset, wireless network adapter are interconnected as a unit

## Slide 16: AMD Processors
Table 4-2 Current AMD processors

## Slide 17: Selecting and Installing a Processor
PC repair technician tasks
  Assemble a PC from parts
  Exchange a faulty processor
  Add a processor
  Upgrade an existing processor
Must know how to:
  Match processor to system
  Install processor on motherboard

## Slide 18: Select a Processor to Match System Needs
First requirement
  Select processor motherboard is designed to support
Select best processor meeting general system requirements and user needs
  May have to sacrifice performance for cost

## Slide 19: Install a Processor
Installing an Intel processor in socket LGA1155
  1. Read motherboard user guide and follow directions
  2. Use a ground bracelet or antistatic gloves
  3. Open the socket by pushing down on socket lever and gently push away from socket
  4. Socket load plate opens
  5. Remove socket protective cover
  6. Remove protective cover from processor
  7. Hold processor with index finger and thumb and align processor in socket using the gold triangle and right-angle mark

## Slide 20
Figure 5-13 Align the processor in the socket using the gold
triangle and the right-angle mark

## Slide 21: Install a Processor
Installing an Intel processor in socket LGA1155 (cont’d):
  8. Ensure the processor is aligned correctly in socket
  9. Return lever to its locked position

## Slide 22: Install a Processor
General step to install a cooler
  1. Understand how cooler posts work
  2. Apply thermal compound if necessary (may be preapplied)
  3. Verify locking pins are turned counter-clockwise as far as they will go
  4. Push down on each locking pin until it pops into the hole
  5. Connect power cord from cooler fan to motherboard
  Check BIOS setup to verify the system recognized processor after system up and running

## Slide 23
Figure 5-21 Verify the CPU is recognized correctly by BIOS setup

## Slide 24: Install a Processor
Installing an Intel processor in socket LGA1366
  Similar to installation of processor in Socket LGA 1155 (some steps may not be repeated)
  1. Open the socket and remove protective cover
  2. Line up processor with two posts on the socket (see Figure 5-25 on next slide)
  3. Lower the socket load plate and return lever to locked position
Verify system works

## Slide 25
Figure 5-25 Orient the processor over the socket so that the notches on each
side of the processor match the posts on each side of the socket

## Slide 26: Install a Processor
Installing an Intel processor in socket LGA775
  1. Push down lever and gently push it away from socket, lift socket load plate and remove socket protective cover
  2. Orient processor so notches on two edges of processor line up with two notches on the socket, place processor in socket
  3. Close the socket cover, push down lever and return it to its locked position
Verify system works

## Slide 27
Figure 5-29 Place the processor in the socket,
orienting the notches on two sides

## Slide 28: Install a Processor
Installing an AMD processor in socket AM2+
  Summary of installation steps
    1. Open the socket lever and remove protective cover
    2. Place processor in the socket
    3. Verify processor pins sitting slightly into the holes
    4. Press the lever down and gently into position
    5. Apply thermal compound and install cooler
    6. Clip into place the clipping mechanism on one side of the cooler
    7. Connect fan power cord to power connection
  Verify system works

## Slide 29: Memory Technologies
Random access memory (RAM)
  Holds data and instructions used by CPU
  Static RAM (SRAM) and dynamic RAM (DRAM)
    Both volatile memory
Figure 5-34 RAM on motherboards today is stored in DIMMs

## Slide 30: Memory Technologies
Variations of DRAM
  DIMM – dual inline memory module
  small outline DIMM (SO-DIMM) – used on laptops
  microDIMMs – used on subnotebook computers
  RIMM and SIMM (outdated)
Differences among DIMM, RIMM, SIMM modules
  Data path width each module accommodates
  How data moves from system bus to module

## Slide 31
Table 4-3 Types of memory modules

## Slide 32
Table 4-3 Types of memory modules (continued)

## Slide 33: DIMM Technologies
DIMM (dual inline memory module)
  64-bit data path
  Independent pins on opposite sides of module
  Older DIMMs
    Asynchronous with system bus
  Synchronous DRAM (SDRAM)
    Runs synchronously with system bus
    Two notches
    Uses 168 pins

## Slide 34: DIMM Technologies
Double Data Rate SDRAM
  Also called DDR SDRAM, SDRAM II, DDR
    Two times faster than SDRAM
  DDR2 SDRAM
    Faster than DDR and uses less power
  DDR3 SDRAM
    Faster than DDR2 and uses less power
  DDR2 and DDR3
    Use 240 pins
    Not compatible: use different notches

## Slide 35: DIMM Technologies
Factors that affect capacity, features, and performance of DIMMS:
  Number of channels they use
  How much RAM is on one DIMM
  Speed
  Error-checking abilities
  Buffering

## Slide 36: DIMM Technologies
Early single channel DIMMs
  Memory controller is accessed one DIMM at a time
Dual channels
  Memory controller communicates with two DIMMs at the same time
    Doubles memory access speed
Triple channels
  Accesses three DIMMs at once
DDR, DDR2, DDR3 DIMMs use dual channels
  DDR3 DIMMs also use triple channels

## Slide 37: DIMM Technologies
Quad channeling
  Introduced with Intel Sandy Bridge chipsets and processors
  Using eight memory slots:
    Processor can access four slots at a time using two different channels
Figure 5-39 The Intel Desktop
Board DX79T0 has eight memory
Slots and supports two quad channels

## Slide 38: DIMM Technologies
Setting up dual channeling
  Pair of DIMMs in a channel must be equally matched
    Size, speed, features
    Use same manufacturer (recommendation)
Figure 5-37 Matching pairs of DIMMs installed in four DIMM slots
that support dual channeling

## Slide 39: DIMM Technologies
Setting up triple-channeling
  Three DIMM slots populated with three matching DDR3 DIMMs
Figure 5-38 Three identical DDR3 DIMMs installed in a triple-channel configuration

## Slide 40: DIMM Technologies
DIMM Speed
  Measured in MHz and PC rating
PC rating
  Total bandwidth between module and CPU
  DDR2 PC rating
    Usually labeled PC2
  DDR3 PC rating
    Usually labeled PC3

## Slide 41: DIMM Technologies
Single-sided DIMM
  Memory chips installed on one side of module
Double-sided DIMM
  Memory chips installed on both sides of module
Memory bank
  Memory processor addresses at one time
  64 bits wide
Dual ranked
  DIMMs providing two or more banks
    Reduces overall memory price at the expense of performance

## Slide 42: DIMM Technologies
Error-correcting code (ECC)
  Detects and corrects error in a single bit
  Application: ECC makes 64-bit DIMM a 72-bit module
Parity
  Error-checking based on an extra (ninth) bit
  Odd parity
    Parity bit set to make odd number of ones
  Even parity
    Parity bit set to make even number of ones
Parity error
  Number of bits conflicts with parity used

## Slide 43: DIMM Technologies
Buffered and registered DIMMs
  Hold data and amplify signal before data written
  Registered DIMM
    Uses registers
  Unbuffered DIMM
    No buffers or register support
  Fully buffered DIMM (FB-DIMM)
    Uses an advanced buffering technique
    Allows servers to support a large number of DIMMs
  Notches on module indicate supported technologies

## Slide 44: DIMM Technologies
CAS latency and RAS latency
  Column access strobe (CAS) latency
  Row access strobe (RAS) latency
    Both refer to number of clock cycles it takes to write or read a column or row of data off a memory module
    CAS latency used more than RAS latency
    Lower values are better than higher
  Memory module ads
    Provide CAS latency value within series of timing numbers
      Example: 5-5-5-15

## Slide 45: RIMM Technologies
Direct Rambus DRAM
  Also known as RDRAM, Direct RDRAM, Rambus
  RIMM memory module
  Expensive and slower than current DIMMs
  RIMMs using 16-bit data bus: two notches, 184 pins
  RIMMs using 32-bit data bus: single notch, 232 pins
C-RIMM (Continuity RIMM)
  Placeholder module
  Ensures continuity throughout all slots
  No memory chip

## Slide 46: Memory Technologies and Memory Performance
Memory performance factors to consider
  Total RAM installed
  Memory technology used
  Speed of memory in MHz, PC rating, or ns
  ECC or non-ECC
  CL or RL rating
  Single, dual, triple or quad channeling
Connectors inside memory slots are tin or gold
  Edge connectors on memory modules follow suit
  Match connectors to prevent corrosive chemical reactions between metals

## Slide 47: How to Upgrade Memory
Basic technique
  Add more RAM modules
Problems solved
  Slow performance
  Applications refusing to load
  An unstable system
  Windows “Insufficient memory” error message

## Slide 48: How to Upgrade Memory
Questions to ask
  How much RAM do I need and how much is currently installed?
  How many and what kind of memory modules are currently installed on my motherboard?
  How many and what kind of modules can I fit on my motherboard?
  How do I select and purchase the right modules for my upgrade?
  How do I physically install the new modules?

## Slide 49: How Much Memory Do I Need and How Much Is Currently Installed?
Best answer: “All you can get”
  Windows 7 requires at least 2 GB RAM
  RAM limit for a 32-bit OS
    4 GB installed RAM

## Slide 50: How Many and What Kind of Memory Modules Are Currently Installed?
Open the case and look at memory slots
  How many slots?
  How many filled?
  Review module imprint
Examine module for physical size and notch position
Read motherboard documentation
  See if board supports dual, triple, or quad channels
Last resort
  Take motherboard and old memory modules to a good computer parts store for confirmation

## Slide 51: How Many and What Kind of Modules Can Fit on My Motherboard?
Read motherboard documentation
  Indicates how much memory motherboard can physically hold
DIMM modules
  DIMMs can be installed as single modules
  Motherboard supporting dual channeling
    Install matching DIMMs in each channel for best performance
  DDR3 board supporting triple channeling
    For best performance install three matching DIMMs in triple-channel slots

## Slide 52: How Many and What Kind of Modules Can Fit on My Motherboard?
Motherboard using DDR3 triple-channel DIMMs
  Use three matching DIMMs in the three blue slots
    If fourth slot populated, board reverts to single channeling
  Dual channeling:
    Install two matching DIMMs in two blue slots farthest from processor
    Leave other two slots empty
  For one installed DIMM:
    Place it in the blue slot farthest position from processor

## Slide 53: How Many and What Kind of Modules Can Fit on My Motherboard?
Motherboard using DDR3 triple-channel DIMMs (cont’d.)
  Follow motherboard documentation
  Serial Presence Detect (SPD)
    Declares module’s size, speed, voltage, and data path width to system BIOS at startup
    Today’s memory always supports SPD

## Slide 54: How Many and What Kind of Modules Can Fit on My Motherboard?
Motherboard using DDR DIMMs with dual channeling
  Allows three different DDR DIMM speeds in one to four sockets, supports dual channeling
  Two blue memory slots and two black slots
  For dual channeling
      Matching DIMMs must be installed in the two blue sockets
  If two DIMMs installed in the two black sockets
      They must match each other

## Slide 55: How Many and What Kind of Modules Can Fit on My Motherboard?
Pentium motherboard using DDR DIMMs
  Example: Motherboard using 168-pin single-sided DIMM modules
  Documentation says to use unbuffered, 3.3-V, ECC, PC100 DIMM SDRAM modules
    PC100: modules should be rated to work with a motherboard running at 100 MHz
  Can choose to use or not use ECC modules
    BIOS setup should show feature disabled
  Three DIMM slots on the board (sockets) hold one bank of memory

## Slide 56: How Many and What Kind of Modules Can Fit on My Motherboard?
RIMM modules
  No longer made
  Replace one or more C-RIMMs with RIMMs
    Match new RIMMs existing RIMMs
    Follow motherboard documentation
  Look at existing modules and motherboard documentation

## Slide 57: How Do I Select and Purchase the Right Memory Modules?
Compromises if exact match not available
  Mixing unbuffered memory with buffered
    Registered memory will not work
  Match memory module manufacturer if possible
    Try using memory from two different manufacturers
  If mixing memory speeds:
    All modules perform at slowest speed

## Slide 58: How Do I Select and Purchase the Right Memory Modules?
Using a web site to research your purchase
  Look for search utility matching modules to board
Figure 5-56 The Kingston web site DIMM recommendations
for a particular motherboard

## Slide 59: How Do I Install the New Modules?
Precautions:
  Always use a ground bracelet
  Turn off power, unplug power cord, press power button, remove case cover
  Handle memory modules with care
  Do not touch metal contacts on memory module or expansion cards
  Do not stack cards or modules
  Look for notches on one side or in the middle for correct orientation

## Slide 60: How Do I Install the New Modules?
Installing DIMMS
  Pull out supporting arms on the sides of the slot
  Use notches on DIMM edge connector as a guide
  Insert DIMM straight down into the slot
  Ensure supporting arms lock into position
New installations are generally uncomplicated
  Usually involve placing memory on motherboard
  Older computers may need change to CMOS setup
  If new memory not recognized try reseating device

## Slide 61: How Do I Install the New Modules?
Installing RIMMS
  Install RIMMs beginning with bank 0, followed by bank 1
  If C-RIMM is already in the slot remove C-RIMM
  Insert module straight down in the socket
  When fully inserted supporting clips should pop back into place

## Slide 62: Summary
Processor: most important motherboard component
  Two major manufacturers are Intel and AMD
Processors are rated by speed of the system bus, the socket and chipset, processor architecture, multi-core rating, internal memory cache, amount and type of RAM and computing technologies
Memory cache inside the processor housing can be L1, L2, and L3 cache
Core of processor has two arithmetic logic units (ALUs) and each core can process two threads at once

## Slide 63: Summary
Current families of Intel processors include Core, Atom, Celeron, and Pentium
Current AMD processor families include FX, Phenom, Athlon, and Sempron
Select a processor that the motherboard supports
When installing, always follow directions in motherboard user guide
DRAM is stored on four kinds of modules: DIMM, SO-DIMM, RIMM, and SIMM modules
DIMMs can be single-sided or double-sided

## Slide 64: Summary
DIMMs can work together in dual, triple, or quad channels
DIMM and RIMM speeds are measured in MHz or PC rating
The memory controller can check memory for errors and possibly correct those errors using ECC
Buffers and registers are used to hold data and amplify a data signal
RIMMs require that every RIMM slot be populated
When upgrading memory, use the type, size, and speed the motherboard supports