## Slide 1: A+ Guide to Managing & Maintaining Your PC, 8th Edition
Chapter 6
Supporting Hard Drives

## Slide 2: Objectives
Learn about the technologies used inside a hard drive and how a computer communicates with a hard drive
Learn how to select and install a hard drive
Learn about tape drives and floppy drives

## Slide 3: Hard Drive Technologies and Interface Standards
Hard disk drive (HDD) or hard drive sizes
  2.5" size for laptop computers
  3.5" size for desktops
  1.8" size for low-end laptops, other equipment

## Slide 4: Technologies Used Inside a Hard Drive
Solid state drive (SSD) or solid state device (SSD)
  No moving parts
  Built using nonvolatile flash memory stored on EEPROM (Electronically Erasable Programmable Read Only Memory) chips
  Memory in an SSD is called NAND flash memory
  Lifespan is based on the number of write operations to the drive
  Expensive technology, but faster, more reliable, last longer, and use less power than magnetic drives

## Slide 5: Technologies Used Inside a Hard Drive
Magnetic hard drive
  One, two, or more platters, or disks
    Stacked together, spinning in unison inside a sealed metal housing
  Firmware controls data reading, writing and motherboard communication
  Read/write heads are controlled by an actuator
  Data is organized in concentric circles, called tracks
    Tracks are divided into segments called sectors
  Most current drives use 4096-byte sectors
Hybrid hard drives use both technologies
  Operating system must support it

## Slide 6
Figure 6-2 Solid-state drives by Toshiba

## Slide 7
Figure 6-3 Inside a magnetic hard drive

## Slide 8
Figure 6-4 A hard drive or floppy disk is divided into tracks and
sectors; several sectors make one cluster

## Slide 9: Technologies Used Inside a Hard Drive
Low-level formatting – sector markings are written to the hard drive at the factory
  Not the same as high-level formatting performed for Operating System installation
Firmware, BIOS and OS use logical block addressing (LBA) to address all hard drive sectors
  Size of each sector + total number of sectors determine drive capacity
S.M.A.R.T – Self-Monitoring Analysis ad Reporting Technology
  Used to predict when a drive is likely to fail

## Slide 10: Interface Standards Used By a Hard Drive
Current internal hard drives methods
  Parallel ATA (PATA) and Serial ATA (SATA)
External hard drive methods
  External SATA (eSATA), SCSI, FireWire, USB, Fibre Channel
Figure 6-5 Timeline of interface standards used by internal drives

## Slide 11: Interface Standards Used by a Hard Drive
Interface standards define data speeds and transfer methods with a computer system
  Also define types of cables and connectors
Standards
  Developed by Technical Committee T13
  Published by American National Standards Institute (ANSI)

## Slide 12
Table 5-1 Summary of ATA interface standards for storage devices

## Slide 13: Parallel ATA or EIDE Drive Standards
Parallel ATA or EIDE drive standards or Integrated Drive Electronics (IDE)
  Allows one or two IDE connectors on a motherboard
    Each use 40-pin data cable
  Advanced Technology Attachment Packet Interface
    Required by optical drives (e.g., CD or DVD)
Types of PATA ribbon cables
  Older cable
    40 pins and 40 wires
  80-conductor IDE cable
    40 pins and 80 wires
  Maximum recommended length of either is 18”

## Slide 14
Figure 6-9 In comparing the 80-conductor cable to the 40-conductor cable, note they are
about the same width, but the 80-conductor cable has many more and finer wires

## Slide 15: Parallel ATA or EIDE Drive Standards
Transferring data between hard drive and memory
  Direct memory access (DMA) transfer mode
    Transfers data directly from drive to memory without involving the CPU
    Seven DMA modes
  Programmed Input/Output (PIO) transfer mode
    Involves the CPU, slower than DMA mode
    Five PIO modes used by hard drives
  Ultra DMA
    Data transferred twice for each clock beat, at the beginning and again at the end

## Slide 16: Parallel ATA or EIDE Drive Standards
Startup BIOS
  Autodetects drive and selects fastest mode that drive and BIOS support
Independent Device Timing
  Motherboard chipset feature
  Supported by most chipsets today
  Allows two hard drives to share same parallel ATA cable but use different standards
  Allows two drives to run at different speeds as long as motherboard supports them

## Slide 17: Serial ATA Standards
Serial ATA standards
  Developed by a consortium of manufacturers
    Serial ATA International Organization (SATA-IO)
  Uses serial data path rather than traditional parallel data path
  Advantages
    Faster than PATA interfaces and used by all drive types
    Multiple connectors are easy to configure
    Supports hot-swapping (hot-plugging)
      Connect and disconnect drive while system is running
    Internal cable length: up 1 meter
    Cable does not hinder airflow (narrower than PATA)

## Slide 18
Figure 6-12 A SATA data cable and SATA power cable

## Slide 19
Table 5-2 SATA Standards

## Slide 20: Serial ATA Standards
Serial ATA standards (cont’d.)
  Motherboard or expansion card can provide external SATA (eSATA) ports for external drives
  External SATA (eSATA)
    eSATA drives use special external shielded serial ATA cable up to 2 meters long
  Purchasing considerations
    SATA standards for the drive and motherboard need to match for optimum speed
    If no match, system runs at the slower speed

## Slide 21: SCSI Technology
Small Computer System Interface standards
  Used primarily in servers
  Support either 7 or 15 devices (standard dependent)
  Provides better performance than ATA standards
SCSI subsystem
  SCSI controller types: embedded or host adapter
  Host adapter supports internal and external devices
  Daisy chain: combination of host adapter and devices
  Each device on bus assigned SCSI ID (0 - 15)
  A physical device can embed multiple logical devices
    Assigned a Logical Unit Number (LUN)

## Slide 22
Figure 6-15 Using a SCSI bus, a SCSI host adapter card can support internal and external SCSI devices

## Slide 23: SCSI Technology
Terminating resistor
  Plugged into last device at end of the chain
  Reduces electrical noise or interference on the cable
Categories of SCSI Standards
  8-bit (narrow SCSI)
    Uses 50-pin SCSI connector (A cable) or 25-pin SCSI connector that looks like a parallel port (DB-25)
  16-bit (wide SCSI)
    Uses 68-pin SCSI connector (P cable)

## Slide 24: SCSI Technology
Various SCSI versions
  SCSI-1, SCSI-2, and SCSI-3
    Also known as regular SCSI, Fast SCSI, Ultra SCSI
Serial attached SCSI (SAS)
  Allows for more than 15 devices on single chain
  Uses smaller, longer, round cables
  Uses smaller hard drive form factors, larger capacities
  Compatible with serial ATA

## Slide 25
Figure 6-18 The most popular SCSI connectors are 50-pin, A-cable connectors
For narrow SCSI and 68-pin, P-cable connectors for wide SCSI

## Slide 26: How to Select and Install Hard Drives
Topics covered
  Selecting a hard drive
  Installation details for SATA drive, IDE drive
  How to install hard drive in a bay too wide for drive
  How to set up a RAID system

## Slide 27: Selecting a Hard Drive
Hard drive must match OS and motherboard
  Need to know what standards the motherboard or controller card providing the drive interface can use
  Consult documentation for the board or card
BIOS uses autodetection to prepare the device
  Drive capacity and configuration selected
  Best possible ATA standard becomes part of configuration

## Slide 28: Selecting a Hard Drive
Considerations:
  Drive capacity
    Today’s desktop hard drives range from 60 GB – 2 TB
  Spindle speed
    Most common is 7200 RPM
    The higher the RPMs, the faster the drive
  Interface standard
    Use standards the motherboard supports
  Cache or buffer size
    Ranges from 2 MB to 64 MB

## Slide 29: Steps to Install a Serial ATA Drive
Some SATA drives have two power connectors
  Choose only one to use
  Never install two power cords at the same time
If you have a SATA drive and a PATA connector (or vice versa)
  Purchase an adapter to make the drive fit the motherboard connection
  Can also purchase a SATA and/or PATA controller card

## Slide 30: Steps to Install a Serial ATA Drive
Step 1: Know your starting point
  How is your system configured?
  Is everything working properly?
  Write down what you know about the system
Step 2: Read the documentation and prepare your work area
  Read all installation instructions first
  Visualize all the steps
  Protect against ESD and avoid working on carpet

## Slide 31: Steps to Install a Serial ATA Drive
Step 2: Read the documentation and prepare your work area (cont’d)
  Handle the drive carefully
  Do not touch any exposed circuitry
  Drain static electricity from the package and from your body by touching metal for at least 2 seconds
  Do not place the drive on the computer case or on a metal table

## Slide 32: Steps to Install a Serial ATA Drive
Step 3: Install the drive
  Turn off the computer and unplug it
  Decide which bay will hold the drive
  Slide drive in the bay and secure it (use two screws on both sides)
  Use correct motherboard serial ATA connector
  Connect a 15-pin SATA or 5-pin Molex power connector from the power supply to the drive
  Check all connections and power up the system
  Verify drive recognized correctly via BIOS setup

## Slide 33: Steps to Install a Serial ATA Drive
Now ready to prepare the hard drive for first use
  Boot from Windows setup CD or DVD
    Follow directions on the screen to install Windows on the new drive
  If installing a second hard drive with Windows installed on first drive use Windows Disk Management utility to partition and format the second drive

## Slide 34: Steps to Install a Serial ATA Drive
Installing a drive in a removable bay
  Unplug the cage fan from its power source
  Turn handle on each locking device counterclockwise to remove it
  Slide the bay to the front and out of the case
  Insert hard drive in the bay
    Use two screws on each side to anchor the drive in the bay
  Slide the bay back into the case
  Reinstall the locking pins

## Slide 35
Figure 6-30 The removable bay has a fan in front and is anchored to the case with locking pins
Figure 6-31 Install the hard drive in the bay using two screws on each side of the drive

## Slide 36: Steps to Configure and Install a Parallel ATA Drive
Configurations for four EIDE devices in a system:
  Primary IDE channel, master device
  Primary IDE channel, slave device
  Secondary IDE channel, master device
  Secondary IDE channel, slave device
Figure 6-35 A motherboard supporting PATA has two IDE channels; each can support a master and slave drive using a single EIDE cable

## Slide 37: Steps to Configure and Install a Parallel ATA Drive
Master or slave designations are made by:
  Setting jumpers or DIP switches
  Use special cable-select data cable
  Color-coded connectors
    Blue end connects to motherboard; black end connects to drive
Figure 6-36 80-conductor cable connectors are color-coded

## Slide 38: Steps to Configure and Install a Parallel ATA Drive
Motherboard color-coding
  Primary channel connector: blue
  Secondary channel connector: black
  Ensures ATA/66/100/133 hard drive installed on the primary IDE channel
Figure 6-37 The primary IDE channel connector is often color-coded as blue

## Slide 39: Steps to Configure and Install a Parallel ATA Drive
Step 1: Open case, decide how to configure drives
Step 2: Set the jumpers on the drive
Figure 6-38 A PATA drive most likely will have diagrams of jumper settings for master and slave options printed on the drive housing

## Slide 40
Table 5-4 Jumper settings on a parallel ATA hard drive
Figure 6-39 Jumper settings on a hard drive and their meanings

## Slide 41: Steps to Configure and Install a Parallel ATA Drive
Step 3: Mount the drive in the bay
  Decide whether to connect data cable before or after inserting bay inside the computer case
    Then install drive in bay and connect the cable in whichever order works best
  Connect data cable to IDE connector on motherboard
  Install a power connection to each drive
  Before replacing case cover verify installation

## Slide 42: Setting Up Hardware RAID
RAID (Redundant Array of Inexpensive Disks)
  Also: Redundant Array of Independent Disks
  A technology that configures two or more hard drives to work together as an array of drives
Why use RAID?
  To improve fault tolerance by writing two copies of it, each to a different hard drive
  To improve performance by writing data to two or more hard drives to that a single drive is not excessively used

## Slide 43: Types of RAID
Spanning – sometimes called JBOD (just a bunch of disks)
  Uses two hard drives to hold a single Windows volume
  When one drive is full, data is written to second drive
RAID 0 – uses two or more physical disks
  Writes to physical disks evenly across all disks so that no one disk receives all activity
  Windows calls RAID 0 a striped volume

## Slide 44: Types of RAID
RAID 1: Mirroring
  Duplicates data on one drive to another drive and is used for fault tolerance (mirrored volume)
RAID 5: uses three or more drives
  Stripes data across drives and uses parity checking
  Data is not duplicated
RAID 10: RAID 1+0 (pronounced RAID one zero)
  Combination of RAID 1 and RAID 0
  Takes at least 4 disks

## Slide 45: How to Implement Hardware RAID
Hardware implementation
  Hardware RAID controller or RAID controller card
    Motherboard does the work, Windows unaware of hardware RAID implementation
Software implementation uses operating system
Best RAID performance
  All hard drives in an array should be identical in brand, size, speed, other features
If Windows installed on a RAID hard drive RAID must be implemented before Windows installed

## Slide 46
Figure 6-45 RAID controller card provides four SATA internal connectors

## Slide 47: How to Implement Hardware Raid
General directions to install RAID 5 array using three matching SATA drives
  Install drives in the computer case and connect each to motherboard
  Boot system and enter BIOS setup
    Verify drives recognized, select option to configure SATA, and select RAID
  Reboot the system
    Press Ctrl and I to enter the RAID configuration utility
  Select option 1 to “Create RAID Volume”
    Select RAID 5 (Parity), stripe size value, volume size
    Create volume

## Slide 48
Figure 6-47 Configure SATA ports on the motherboard to enable RAID
Figure 6-48 BIOS utility to configure a RAID array

## Slide 49
Figure 6-49 Make your choices for the RAID array

## Slide 50: About Tape Drives and Floppy Drives
Tape drives can use a SATA, PATA, or SCSI interface
As a technician, you may be called on to support old floppy drives
Both tape drives and floppy drives are covered in this section

## Slide 51: Installing Tape Drives and Selecting Tape Media
Tapes drives – an inexpensive way of backing up a hard drive
WORM (write once read many) – assures data written will not be deleted or overwritten
Disadvantage: data is stored by sequential access
  To read data from anywhere on the tape, you must start at the beginning of the tape and read until you find the data you want
  Slow and inconvenient

## Slide 52: Installing Tape Drives and Selecting Tape Media
Two kinds of tapes:
  Full-sized data cartridges
  Minicartridges
    More popular because their drives can fit into a standard 3-inch drive bay of a PC case
When selecting a tape drive, consider:
  How many and what type of cartridges the drive can use
  How it interfaces with the computer
External drives can connect to a computer using a USB, FireWire, SCSI, SAS, or eSATA port

## Slide 53: Installing a Floppy Drive
Floppy disk drive (FDD)
  3 ½” floppy disk format
  Holds only 1.44 MB of data
  Floppy drive subsystem
    Floppy drive, ribbon cable, power cable, connections
    Today’s floppy drive cables have a connector at each end to accommodate a single drive
    Older cables have an extra connector or two in the middle of the cable for a second floppy drive

## Slide 54: Installing a Floppy Drive
Install the drive in a bay as you would a hard drive
Connect floppy drive data cable and power cord to motherboard
  If you connect the cable the wrong way, the drive light will stay lit and will not work
  Be sure the end of the cable with the twist connects to the drive and the other end to the motherboard
Replace cover, turn on computer, and enter BIOS setup to verify installation

## Slide 55: Summary
A hard disk drive (HDD) comes in 3.5” for desktop and 2.5” for laptops
A hard drive can be magnetic, solid-state, or hybrid
Most hard drives use the ATA interface standards
Two ATA categories are parallel ATA and serial ATA
S.M.A.R.T is a self-monitoring technology whereby the BIOS monitors the health of a hard drive
SCSI interface standards include narrow and wide SCSI and can use a variety of cables and connectors

## Slide 56: Summary
When selecting a hard drive, consider storage capacity, technology, spindle speed, interface standard, and buffer size
SATA drives require no configuration and are installed using a power cord and a data cable
PATA drives require you to set a jumper to determine if the drive will be the single drive, master, or slave on a single cable
RAID technology uses an array of hard drives to provide fault tolerance and/or improvement in performance

## Slide 57: Summary
Hardware RAID is implemented using the motherboard BIOS or a RAID controller card
Software RAID is implemented in Windows
Tape drives are an inexpensive way to back up an entire hard drive or portions of it
Today’s floppy disks are 3.5” high-density disks that hold 1.44 MB of data
After a floppy disk drive is installed, you must configure the drive in BIOS setup