## Slide 1: A+ Guide to Managing & Maintaining Your PC, 8th Edition
Chapter 13
Troubleshooting Hardware Problems

## Slide 2: Objectives
Learn how to approach and solve a computer problem related to hardware, especially when the problem occurs during the boot
Learn how to troubleshoot problems with the electrical system
Learn how to troubleshoot problems that occur during POST before video is active
Learn how to troubleshoot error messages that occur during the POST

## Slide 3: Objectives
Learn how to troubleshoot problems with the motherboard, processor, and RAM
Learn how to troubleshoot hard drive problems
Learn how to troubleshoot problems with the monitor and video
Learn about protecting a computer and the environment

## Slide 4: How to Approach A Hardware Problem
First step: Interview the customer
Include these questions:
  Can you describe the problem, when did it first start, and when does it occur?
  Was the computer recently moved?
  Was any new hardware or software recently installed?
  Was any software recently reconfigured or upgraded?
  Did someone else use your computer recently?

## Slide 5: How to Approach A Hardware Problem
Include these questions (cont’d):
  Does the computer have a history of similar problems?
  Is there important data on the drive that is not backed up?
  Can you show me how to reproduce the problem?
After gathering information:
  Prioritize what to do and begin diagnosing and addressing the problem

## Slide 6: How to Approach A Hardware Problem
Troubleshooting resources:
  User manuals
  Internet
  Chat, telephone, or email technical support
  Manufacturer’s diagnostic software
  Technical associates in your organization
Technicians need a game plan on how to solve PC problems
  The flowchart on the following slide is a great example

## Slide 7
Figure 13-2 Use this flowchart when first facing a computer problem

## Slide 8: How to Approach A Hardware Problem
On a computer that is not booting properly:
  If the hard drive has important data on it, consider moving the hard drive to a working computer as a second drive
  No need to install the drive in a bay, just connect it with a data cable and power cable
  Use Windows Explorer to copy files from non-booting drive to the hard drive of the working computer
  Return drive to the original system and continue trying to solve the original problem

## Slide 9
Figure 13-4 A POST error message on a black screen shown early in the boot

## Slide 10
Figure 13-5 Move a hard drive to a working computer to recover data on the drive

## Slide 11
Figure 13-6 Use an IDE-to-USB converter for diagnostic testing and to
recover data from a failing PATA hard drive

## Slide 12: Troubleshooting the Electrical System
Electrical problems can:
  Occur before or after the boot
  Be consistent or intermittent
Possible symptoms of electrical problem:
  PC appears to be “dead”
  PC sometimes locks up during booting
  Error codes or beeps occur during booting
  Smell burnt parts or odors
  PC powers down at unexpected times
  PC appears dead except you hear a whine coming from the power supply

## Slide 13: Troubleshooting the Electrical System
Try these simple things first:
  If you small any burnt part, don’t turn system on
    Find burnt up part and replace
  If power supply is whining, don’t turn system on
    Open case and look for short or consider upgrading
    Test power supply with a power supply tester
  Check power cord connection and power bar it may be plugged into
  Is power outlet controlled by wall switch? If so, turn it on
  Are any cable connections loose?

## Slide 14: Troubleshooting the Electrical System
Try these simple things first (cont’d):
  Is the circuit breaker blown? Is the house circuit overloaded?
  Are all switches on the system turned on?
  Is it possible the system has overheated? If so, wait awhile and try again
  Older computers might be affected by electromagnetic interference (EMI)
    Check for sources of EMI such as fluorescent lighting or an electric fan or copier sitting near PC

## Slide 15: Problems That Come and Go
Generally, intermittent problems are more difficult to solve
Symptoms of what may be an intermittent problem:
  Computer stops or hangs for no reason
  Memory errors appear intermittently
  Data is written incorrectly to the hard drive
  Keyboard stops working at odd times
  Motherboard fails or is damaged
  Power supply overheats and becomes hot to touch
  Power supply fan whines and becomes noisy

## Slide 16: Power Problems With the Motherboard
Short might occur if a motherboard component makes improper contact with the chassis
  Can seriously damage the motherboard
  Check for missing/loose standoffs or loose screws
Shorts in motherboard circuits might also cause problems
  Look for damage on the bottom of the motherboard
  Look for burned-out capacitors that are spotted brown or corroded

## Slide 17: Problems With Overheating
Symptoms of overheating:
  System hangs or freezes at odd times or after the boot starts
  Windows BSOD (blue screen of death) error occurs during the boot
  You cannot hear a fan running or the fan makes a whining sound
  You cannot feel air being pulled into or out of the case
You can purchase a temperature sensor that will sound an alarm when the inside of the case is too hot

## Slide 18: Problems With Overheating
Things to do to solve overheating:
  If system hangs, go into BIOS setup and find the CPU screen that reports temperature (should not exceed 38 degrees C)
  Use compressed air, a blower, or antistatic vacuum to remove dust from the power supply and vents
  Check airflow inside the case to see if fans are running (may need to replace a fan)
  Install extra fans if case will hold them
  Can the side of the case hold a chassis air guide that guides air to the processor? If so, install one

## Slide 19
Figure 13-9 Dust in the cooler fan can cause the fan to fail and the
processor to overheat

## Slide 20
Figure 13-10 Install one exhaust fan on the rear of the case
to help pull air through the case

## Slide 21: Problems With Overheating
Things to do to solve overheating (cont’d):
  To improve airflow, replace missing faceplates and expansion slot covers
  Ensure cables are not in the way of airflow
  Place case so that there are a few inches of space on both sides and the top of the case
  Verify the cooler is connected properly to the processor
  After closing the case, leave system off for at least 30 minutes

## Slide 22
Figure 13-11 For optimum airflow, don’t leave empty expansion
slots and bays uncovered

## Slide 23
Figure 13-12 Use cable ties to hold cables out of the way of fans and airflow

## Slide 24: Problems With Overheating
Things to do to solve overheating (cont’d):
  Check BIOS setup to see if the processor is being overclocked (can cause system to overheat)
  Have too many peripherals been installed inside the case? Try to leave an empty slot between each card
  Flash BIOS to update firmware on motherboard
  Replace thermal compound if it has hardened

## Slide 25
Figure 13-14 Vents and fans need to be arranged for best airflow

## Slide 26: Problems With Overheating
Use a power supply that has vents on the bottom and front for better ventilation
Figure 13-15 This power supply has vents on the bottom to
provide better airflow inside the case

## Slide 27: Troubleshooting POST Before Video Is Active
If power is getting to system, but screen is blank:
  Turn off and then back on
  Listen carefully to any beep codes or BIOS speech messages
  One beep or no beep indicates all is well
  If you hear more than one beep
    Look up beep code in the motherboard or BIOS documentation

## Slide 28
Table 8-2 Common beep codes and their meanings for Intel and Award BIOS

## Slide 29: Troubleshooting Error Messages During the Boot
If video and electrical systems are working
  Most boot problems show up as an error message on the screen
  Error messages that occur before Windows starts to load usually apply to hardware components
  See table on following slide
If Windows boot manager program has problems loading Windows
  Different set of error messages will be displayed

## Slide 30
Table 8-3 Error messages that occur before Windows starts

## Slide 31
Figure 13-17 A Windows error early in the boot that is related to software

## Slide 32: Troubleshooting the Motherboard, Processor, and RAM
Symptoms that a motherboard, processor, or memory is failing:
  System begins to boot put then powers down
  Error message is displayed during the boot
  System becomes unstable, hangs, or freezes at odd times
  Intermittent Windows or hard drive errors occur
  Components on the motherboard or devices connected to it don’t work
Check simple things first

## Slide 33: Troubleshooting the Motherboard, Processor, and RAM
Follow these steps to find source of problem:
  1. The problem might be a virus
    Run antivirus software to check for viruses
  2. A memory module might be failing
    Use Memory Diagnostics tool to test memory
  3. Check for potential hardware problems using Device Manager
  4. Download and install any Windows updates or patches
  5. If problem began after a change or new install, uninstall device or application

## Slide 34: Troubleshooting the Motherboard, Processor, and RAM
Follow these steps to find source of problem (cont’d):
  6. Use System window to find out how much RAM is installed (consider upgrading if not enough)
  7. Check BIOS setup to ensure proper settings
  8. Disable any quick booting features in BIOS
    Then look for errors reported during the boot
  9. Flash BIOS to update firmware on the board
  10. Check CD that came with motherboard
    May have diagnostic tests
  11. Update all drivers of motherboard components that are not working

## Slide 35: Troubleshooting the Motherboard, Processor, and RAM
Follow these steps to find source of problem (cont’d):
  12. If an onboard port is not working:
    Verify the problem is not with the device using the port
    Go into BIOS setup and verify the port is enabled
    Check Device Manager and verify Windows recognizes port with no errors
    Update motherboard drivers for this port from manufacturer’s web site
    Use a loop-back plug to test the port
    Disable the port in BIOS setup and install an expansion card

## Slide 36: Troubleshooting the Motherboard, Processor, and RAM
Follow these steps to find source of problem (cont’d):
  13. Suspect the problem is a failing hard drive
  14. Suspect the problem is caused by overheating
  15. Search the support section of the web sites
  16. Verify the installed processor is supported by the motherboard

## Slide 37: Problems With Installations
If new processor, DIMM, or other component has been installed and system does not boot:
  1. Check simple things first
    Check all power and data connections
  2. Open case and check installation of the new component
  3. Reboot the system
    If problem still occurs, make sure new component is compatible with system

## Slide 38: Problems With Installations
If new processor, DIMM, or other component has been installed and system does not boot (cont’d):
  4. Try taking out new component and checking for physical defects (bent pins on processor)
  5. Is case getting too hot?
  6. Clean edge connectors on memory or expansion cards (blow out any dust from inside case)
  7. When upgrading processor
    Reinstall old processor, flash BIOS and try the new processor again

## Slide 39: Troubleshooting Hard Drives
Problems caused by hard drive during the boot can be caused by:
  Hard drive subsystem
  File system on the drive
  Files required by Windows when it begins to load
Hardware problems usually show up at POST
Could be due to :
  The drive, data cable, electrical system, motherboard, SCSI host adapter

## Slide 40: Troubleshooting Hard Drives
Things to do and check before opening case:
  Check to see if BIOS displays a numeric error code or other message during POST
  Check BIOS setup for errors in the hard drive configuration
  Try booting from another bootable media
  For a RAID array, use the firmware utility to check the status of each disk in the array and check for errors

## Slide 41: Troubleshooting Hard Drives
If the problem is still not solved, open case and check these things:
  Remove and reattach all drive cables
  If using a RAID, SATA, PATA, or SCSI controller card, remove and reseat it or place in a different slot
  Check jumper settings on IDE drives
  Inspect drive for damage
  Determine if hard drive is spinning by listening to it
  Check the cable for frayed edges
  Check installation manual

## Slide 42: Troubleshooting Hard Drives
If the problem is still not solved, open case and check these things (cont’d):
  Use Windows tools for checking a hard drive
  Check the drive manufacturer’s web site for diagnostic software
  Move the device to a working computer and install it as a second drive
  Exchange the three field replaceable units
    Reconnect or swap the data cable
    Reseat or exchange the controller card
    Exchange the hard drive for a known good drive

## Slide 43: Troubleshooting Hard Drives
If the problem is still not solved, open case and check these things (cont’d):
  If your drives whines loudly, try replacing it
  A bad power supply or a bad motherboard also might cause a disk boot failure

## Slide 44: Troubleshooting Monitors and Video
For monitor and video problems:
  Try easy things first such as:
    Check cable connections
    Check contrast/brightness adjustments

## Slide 45: Monitor Indicator Light Is NOT On; No Image On-Screen
Ask these questions and try:
  Is the monitor power cable plugged in?
  Is the monitor turned on?
  Is the monitor cable plugged into the video port at the back of the PC?
  Try a different monitor and a different monitor cable

## Slide 46: Monitor Indicator Light IS On; No Image On-Screen
Try the following:
  Ensure video cable is securely connected
  If monitor displays POST but goes blank when Windows starts to load:
    Problem is with Windows, not monitor
  Ensure monitor is set to correct voltage (110 vs. 220)
  Might be problem with video card
  Verify video cable connection inside case
  Check the contrast adjustment
  Check brightness or backlight adjustment

## Slide 47: Monitor Indicator Light IS On; No Image On-Screen
Try the following:
  Switch out monitor-to-computer cable
  Test a monitor you know is good on the computer you suspect is bad
  Open computer case and reseat video card
  Trade a good video for suspected bad video card
  Test the RAM on the motherboard
  Try using a backup PCI video card if using a PCI-Express or AGP video card
  Trade the motherboard for one you know is good

## Slide 48: Monitor Indicator Light IS On; No Image On-Screen
Try the following (cont’d):
  For notebook computers, is the LCD switch turned on?
  For notebook computers, try connecting a second monitor to the notebook and use the function key to toggle between the LCD panel and second monitor

## Slide 49: Poor Display
Solve these problems by using controls on the monitor and Windows settings - Do the following:
  LCD monitor controls – usually located on front of monitor
  Windows display settings – use to adjust font size, screen resolution, brightness, color, and Clear Type text
  Update video drivers

## Slide 50: Problems With CRT Monitors
If monitor flickers, has wavy lines or a distorted image, try the following:
  Monitor flicker can be caused by poor cable connections
  Odd-colored blotches or screen flicker can be result of EMI
  Use degauss button to eliminate accumulated or stray magnetic fields
  Change refresh rate to the highest value supported
  Consider purchasing a newer monitor

## Slide 51: Display Settings Make the Screen Unreadable
Return to standard VGA settings called VGA mode
Do the following:
  Reboot the system and press F8 to get to Advanced Boot Options menu
  Select Safe Mode to boot up with minimal configuration of Windows
  After you have changed display settings, restart Windows

## Slide 52: Protecting A Computer and The Environment
Avoid future problems by protecting your computer against environmental factors such as:
  Humidity
  Dust
  Out-of-control electricity
Technicians must learn how to properly dispose of used computer equipment

## Slide 53: Physically Protect Your Equipment
Do’s and Don’ts to protect a computer:
  Do not move or jar computer when on
  Protect a computer against dust and other airborne particles
  Allow for good ventilation inside and outside the system
Figure 13-39 This dust-jammed case fan caused a system to overheat

## Slide 54: Physically Protect Your Equipment
Do’s and Don’ts to protect a computer (cont’d):
  High temperatures and humidity can be dangerous
  Use BIOS setup to disable ability to write to the hard dive boot sector
  Protect your CDs, DVDs, BDs, and other storage media
  Don’t leave a computer turned off for weeks or months at a time
  Do not unpack and turn on a cold computer
  Protect electrical equipment from power surges
    Use uninterruptible power supply (UPS) to protect against power surges, brownouts, or sags

## Slide 55: Document Preventative Maintenance
Keep a record book for each new computer
  Record any changes in setup data and any problems or maintenance
  Keep a record of all changes to BIOS setup data and jumpers on the motherboard
Label documentation and keep in a safe place

## Slide 56: How to Dispose Of Used Equipment
First check to see if any equipment can be donated or at least recycled
If computer is to be given away
  Uninstall any applications software
  Delete private data (use a zero-fill utility)
If trashing a computer
  Use a degausser to erase everything on a magnetic hard drive or drill holes through the drive
  Comply with local government regulation when disposing of any type of equipment

## Slide 57: How to Dispose Of Used Equipment
Table 8-4 Computer parts and how to dispose of them

## Slide 58: Summary
Always begin troubleshooting my interviewing the user
Decide if problem occurs before or after a successful boot and if it is caused by hardware or software
Listen for spinning fans or drives and look for indicator lights to ensure a system is getting power
Removing dust from a system, providing for proper ventilation, and installing extra fans can help keep a system from overheating

## Slide 59: Summary
BIOS gives beep codes when a POST error occurs during the boot before it tests video
Error messages on a black screen during the boot are usually put there by startup BIOS during the POST
The motherboard, processor, RAM, processor cooler assembly, and CMOS battery are field replaceable units
Problems caused by the hard drive during a boot can be caused by the hard drive subsystem, file system, or by files required by Windows to load

## Slide 60: Summary
Video problems can be caused by the monitor, video cable, video card, onboard video, video drivers, or Windows display settings
A CRT monitor might have a degauss button to eliminate stray EMI
Protect a computer against dust and other airborne particles using protective enclosures and air filters, and ridding the inside of a computer from dust
Dispose of used equipment and consumables according to local government environmental guidelines