## Slide 1: A+ Guide to Managing & Maintaining Your PC, 8th Edition
Chapter 14
Troubleshooting Windows Startup Problems

## Slide 2: Objectives
Learn about the boot process from the time you press the power button until the Windows desktop loads
Learn about Windows tools that can help when solving Windows startup problems
Learn how to troubleshoot Windows startup problems

## Slide 3: Understanding The Boot Process
Choosing between a hard boot and a soft boot
  Hard boot (cold boot): turning on the power with the on/off switch
    Takes more time than a soft boot
    Initializes the processor and clears memory
  Soft boot (warm boot): using the OS to reboot
    To save time use the soft boot to restart
    If a soft boot doesn’t work, use a hard boot

## Slide 4: Startup BIOS Controls The Beginning Of The Boot
Startup BIOS: responsible for getting a system up and running
A successful boot depends on the hardware, the BIOS, and the OS performing without errors
Startup BIOS is responsible for:
  Reads motherboard settings and runs the POST
  Setup BIOS might be run (if key is pressed to request)
  Startup BIOS searches for a bootable device

## Slide 5
Figure 14-2 Use BIOS setup screens to change the
hardware configuration for a system

## Slide 6: Steps To Start Windows 7/Vista
The following table lists the components and files necessary to start Windows 7/Vista
Table 6-1 Software components and files needed to start Windows 7/Vista

## Slide 7
Table 6-1 Software components and files needed to start Windows 7/Vista (continued)

## Slide 8
Figure 14-3 Steps to booting the computer and loading Windows 7/Vista

## Slide 9
Figure 14-4 Steps to complete loading Windows 7/Vista

## Slide 10: Windows 7/Vista Tools for Solving Startup Problems
Windows tools to solve startup problems
  Advanced Boot Options menu
  Windows Recovery Environment (Windows RE)
  Command prompt window in Windows RE

## Slide 11: Advanced Boot Options Menu
Press F8 as Windows loads
Repair Your Computer
  Only available in Windows 7
  Launches Windows Recovery Environment
Safe Mode boots a minimum configuration OS
  Uses default system services
  No network access
  Uses a plain video driver
  “Safe Mode” appears in four corners of the screen
  Screen resolution: 800 x 600
  Desktop wallpaper (background): black

## Slide 12
Figure 14-11 Safe Mode loads a minimum Windows configuration

## Slide 13: Advanced Boot Options Menu
Recovering the system using Safe Mode
  Use System restore
  Scan system for virus and run Memory Diagnostics and Chkdsk
  Use Device Manager to uninstall, disable a device with problems, or roll back a driver
  Use System Configuration (Msconfig) to disable unneeded services or startup processes
  Use Programs and Features window to uninstall software
  Use Event Viewer to find information about previously failed startups

## Slide 14: Advanced Boot Options Menu
Tips about loading Safe Mode
  Form Advanced Boot Options menu
    First, try Safe Mode with Networking
    Next, try Safe Mode
    Then, try Safe Mode with Command prompt
  Safe Mode won’t load if core Windows components are corrupted
  When loading Windows in Safe Mode
    All files used for the load are recorded in Ntbtlog.txt file
    File might identify service, device driver, or application loaded at startup causing a problem

## Slide 15: Advanced Boot Options Menu
Safe mode with networking
  Use when solving a problem with booting and network access is needed
  Also use when the Windows installation files are available on the network
Safe mode with command prompt
  Use the sfc /scannow command to verify system files
  Use the chkdsk /r command to check for file system errors
  If problem not solved, launch System Restore

## Slide 16
Figure 14-12 SFC finds and repairs corrupted system files

## Slide 17
Figure 14-13 Use System Restore after booting to
Safe Mode with Command Prompt

## Slide 18: Advanced Boot Options Menu
Enable boot logging
  Windows loads normally with regular desktop
  All files used during load process are recorded
    C:\Windows\Ntbtlog.txt
Figure 14-14 Sample Ntbtlog.txt file

## Slide 19: Advanced Boot Options Menu
Enable low-resolution video (640x480)
  Used when video setting does not allow screen to display clearly to fix a bad setting
  Windows XP, option is called “Enable VGA Mode”
Last known good configuration
  Saved in registry after each successful logon
  Can undo a bad installation and solve the problem
  Try the Last Known Good early in troubleshooting, before it’s overwritten
    When logging onto the system in Safe Mode, the Last Known Good not saved

## Slide 20: Advanced Boot Options Menu
Directory services restore mode (Windows Domain controllers only)
  Used as one step in the process of recovering from a corrupted Active Directory
Debugging mode
  Can move system boot logs from failing computer to another computer for evaluation
Disable automatic restart on system failure
  Stop rebooting upon encountering a system failure

## Slide 21: The Windows Recovery Environment (Windows RE)
Operating system launched from the Advanced Boot Options menu
  Provides graphical and command-line interfaces
To launch Windows RE
  Boot from Windows 7 or Vista setup DVD, and select language preference
  In Windows 7, it is installed on the hard drive and available from the Advanced Boot Options menu
  A Windows 7 system repair disc can be created and can be used to launch Windows RE

## Slide 22
Figure 14-15 Use Backup and Restore to create a system repair disc to use instead of Windows setup DVD

## Slide 23: The Windows Recovery Environment (Windows RE)
After Windows RE is launched the System Recovery Options box offers several recovery tool options
Figure 14-18 Recovery
Tools in Windows RE
for Windows 7

## Slide 24: The Windows Recovery Environment (Windows RE)
Use the least intrusive tools first
Use these Windows RE tools in the order listed:
  1. Startup Repair – least intrusive
    Does not change data or installed applications
Figure 14-20 Startup
Repair suggests you
use System Restore

## Slide 25: The Windows Recovery Environment (Windows RE)
Use these Windows RE tools in the order listed:
  2. Windows Memory Diagnostic
    Use if memory is suspected to be a problem
  3. System Restore
    Can sometimes fix a problem with a corrupted device driver, corrupted Windows settings, or corrupted programs
  4. Command Prompt
    Use this option to run chkdsk or restore a corrupted registry from the Command Prompt window
  5. System Image Recovery – last resort
    Will erase everything and restore previous image

## Slide 26: The Windows Recovery Environment (Windows RE)
In Vista, the Complete PC Restore option is available instead of the Windows 7 option of System Image Recovery
Figure 14-23 Recovery
Tools in Windows RE for
Windows Vista

## Slide 27: The Command Prompt Window in Windows RE
Use when graphical tools available in Windows RE fail to solve the problem
  Offers full read and write access to all files on the drives
Repair a hard drive or other drive
  Use chkdsk and format commands to repair a drive
  Use diskpart to manage hard drives, partitions, and volumes
    Refer to table on the next slide which lists important diskpart commands

## Slide 28
Table 6-2 Important diskpart commands used at the DISKPART> prompt

## Slide 29
Figure 14-24 Use commands in diskpart to partition and format a USB flash drive

## Slide 30: The Command Prompt Window in Windows RE
Enable networking
  Networking is not normally available
  Use the wpeinit command to enable networking
Repair the file system and key boot files
  Use the bootrec command to repair the BCD and boot sectors
  Use the bcdedit command to manually edit the BCD
  Use the bootsect command to repair a dual boot system

## Slide 31
Table 6-3 Commands used in the command prompt window of Windows
RE to repair system files and the file system

## Slide 32: The Command Prompt Window in Windows RE
Manage data files and system files
  Use cd, copy, rename, and delete commands
  Restore registry files using those saved in the RegBack folder
  After each fix, reboot the system to see if problem was solved
  Use commands in Table 6-4 (see next slide) to restore registry files

## Slide 33
Table 6-4 Steps to restore the registry files

## Slide 34: Troubleshooting Windows 7/Vista Startup
To determine where in the boot process the failure occurred, focus on three startup stages of the boot
  Stage 1: Before the progress bar
  Stage 2: After the progress bar and before logon
  Stage 3: After logon

## Slide 35: Problems At Stage 1: Before The Flag Or Progress Bar Appears
Problems might be caused by hardware or startup files
Is the screen blank? If nothing is on the screen:
  Monitor LED light lit
    Reboot, check monitor power, and that it is on
  Monitor LED light is not lit
    Verify system power, monitor is plugged in and on
  If hard drive is not spinning suspect no power is getting to system
    Verify system not in standby mode or hibernation
  Trade monitor for a good one

## Slide 36: Problems At Stage 1: Before The Flag Or Progress Bar Appears
Does the computer appear to have power?
  Can’t hear spinning drive or see lights on case front
    Suspect electrical system
    Check power connections and switches
    May have bad power supply
    Loose connections inside case

## Slide 37: Problems At Stage 1: Before The Flag Or Progress Bar Appears
Does an error message appear before Windows starts?
  BIOS displays error message on-screen if problem is detected
    Uses beeps or speech if video not working
  On-screen messages for nonessential hardware
    Try to bypass error by pressing a key and moving forward in the boot
  On-screen messages for essential hardware
    Focus attention on the error message, beep code, and voice message describing problem

## Slide 38
Figure 14-25 This error message at POST indicates a hardware problem

## Slide 39: Problems At Stage 1: Before The Flag Or Progress Bar Appears
Can startup BIOS access the hard drive?
  Possible messages
    Hard drive not found
    Fixed disk error
    Disk boot failure, insert system disk and press enter
    No boot device available
  Check for physical problem
    Drive, data cable, power, motherboard
  Verify BIOS detected drive correctly
    Turn on autodetection and reboot
  Power down system, unplug it, and physically inspect

## Slide 40: Problems At Stage 1: Before The Flag Or Progress Bar Appears
Can startup BIOS access the hard drive? (cont’d.)
  BIOS found hard drive, but could not read drive
    A disk read error occurred
    Drive not recognized
    Invalid boot disk
    Inaccessible boot device
    Invalid drive specification
    Invalid partition table
    Operating system not found
    Could not find bootmgr or bootmgr missing
  Boot from Windows setup DVD (see next slide)

## Slide 41: Problems At Stage 1: Before The Flag Or Progress Bar Appears
Use BIOS setup to set the boot sequence
  Access BIOS setup utility
  Find screen to change boot sequence
  Make sure DVD drive is listed before hard drive
    Force system to boot from Windows Vista setup DVD
  Save settings and exit BIOS setup

## Slide 42
Figure 14-26 Set the boot order in BIOS setup

## Slide 43: Problems At Stage 1: Before The Flag Or Progress Bar Appears
Can you boot from the Windows setup DVD?
  If not then study error messages, and solve immediate hardware problem
    Hard drive and optical drive might have failed
    Try a bootable USB flash drive
    Successful boot from flash drive indicates problem with both the hard drive and DVD drive
  If able to boot from Windows DVD
    Windows logon screen appears
    Problem isolated to the hard drive

## Slide 44: Problems At Stage 1: Before The Flag Or Progress Bar Appears
Can Windows RE find the Windows installation?
  Launch Windows RE
    Windows RE attempts to locate Windows installation on the hard drive
  If Windows RE cannot locate the installation, but BIOS setup recognizes the drive
    Drive partitions and file systems might be corrupted
  If Windows RE does locate the installation
    Problem likely limited to corrupted or missing system files or drivers
  Attempt fixes: restart system after each step

## Slide 45: Problems At Stage 1: Before The Flag Or Progress Bar Appears
Can Windows RE find the Windows installation? (cont’d.)
  Run Startup Repair
    Sometimes fixes drastic problems with system files, boot records
  Run System Restore
    Process won’t help if file system corrupted
  Restart system and launch Advanced Boot Options menu
    No boot menu: problem may be corrupted boot sector
    Boot menu appears: probable BCD file or other startup file problem

## Slide 46: Problems At Stage 1: Before The Flag Or Progress Bar Appears
Can Windows RE find the Windows installation? (cont’d.)
  Restart system, launch Advanced Boot Options menu (cont’d.)
    If boot menu appears: enable boot logging and reboot
    Check boot log (\Windows\ntbtlog.txt) for the last entry
    Might indicate which system file missing or corrupt
  If boot menu does not appear:
    Return to Windows RE, launch command prompt window, and attempt to repair boot sector

## Slide 47: Problems At Stage 1: Before The Flag Or Progress Bar Appears
Can Windows RE find the Windows installation? (cont’d.)
  If boot menu does appear:
    Return to Windows RE, launch command prompt window, and attempt to repair the BCD file
  Try to repair corrupted file system
    Use command prompt window and chkdsk c: /r command
  When startup files missing or corrupt
    Windows may display an error message

## Slide 48
Figure 14-28 Windows might display a screen similar to this one when a
critical startup file is missing or corrupt

## Slide 49: Problems At Stage 1: Before The Flag Or Progress Bar Appears
Can Windows RE find the Windows installation? (cont’d.)
  Use command prompt window to access drive C
    Get to C prompt: use DIR command to list folders and files
    Good list: check log file for clues
    Not a good list: most likely Vista installation destroyed beyond repair
    Make every effort to copy data to another media

## Slide 50: Problems At Stage 1: Before The Flag Or Progress Bar Appears
Options to recover from a corrupted Windows installation
  Option 1: Complete PC backup available
    Restore system to last backup
  Option 2: Complete PC backup not available and data backups available on hard drive
    Install Windows, format hard drive during installation, install all applications again, restore data
  Option 3: Complete PC backup and data backup not available
    Try to copy data to removable device and reinstall Windows

## Slide 51: Problems At Stage 1: Before The Flag Or Progress Bar Appears
Steps to reinstall Windows
Follow these steps when OS refuses to boot and important data on the drive:
  Boot from Windows setup DVD
    Follow directions on-screen to install the OS
  If you suspect hard drive might be failing, reformat the hard drive and reinstall Windows
  If you suspect a healthy hard drive
    Run Chkdsk to fix errors
    Install all applications and device drivers
    Create all user accounts and customize Vista settings
    Delete the \Windows.Old folder

## Slide 52: Problems At Stage 2: After The Flag Or Progress Bar Appears/Before Logon
Microsoft progress bar appears during the boot
  Windows kernel loaded successfully
  Critical drivers and services configured to be started by the kernel running
  Session Manager (Smss.exe) running in user mode started the Win32 subsystem
  If logon screen not displayed:
    Probable corrupted driver or service started after kernel finished its part of the boot
    Fix by isolating and disabling Windows component, service, or application causing trouble

## Slide 53: Problems At Stage 2: After The Flag Or Progress Bar Appears/Before Logon
Follow these steps:
  1. Launch Advanced Boot Options and try to boot into Safe Mode
    Immediately run antivirus software
    Run Chkdsk c: /r
    Examine all logs in Event Viewer
    Use MSconfig to stop applications just installed, then uninstall and reinstall
    Use System Information (msinfo32.exe)
    Use Device Manager to check for hardware errors
    Use the System File Checker (SFC) tool
    Rename the \Windows\Ntbtlog.txt file

## Slide 54: Problems At Stage 2: After The Flag Or Progress Bar Appears/Before Logon
Follow these steps: (cont’d)
  2. If cannot boot into Safe Mode, select Last Known Good Configuration on the Advanced Boot Options menu
  3. Launch Windows RE and run Startup Repair from the System Recovery Options menu
  4. In Windows RE, run System Restore
    Select the latest restore point
    If that doesn’t fix the problem, try an earlier one
  5. Boot to Advanced Boot Options menu and select Enable Boot Logging

## Slide 55: Problems At Stage 2: After The Flag Or Progress Bar Appears/Before Logon
Follow these steps: (cont’d)
  6. Compare the Ntbtlog.txt file to one that was created in Safe Mode to find what caused error
  7. If you can boot into Safe Mode, use Device Manager to disable the device or use Services console to disable the service
  8. If you cannot boot into Safe Mode, open command prompt window in Windows RE
    Back up registry, find key that loads services and drivers

## Slide 56: Problems At Stage 2: After The Flag Or Progress Bar Appears/Before Logon
Follow these steps: (cont’d)
  9. Disable service or driver by changing Start value to 0x4
    Reboot, replace program file, and restart service or driver

## Slide 57: Problems At Stage 3: After Windows Logon
Problems caused by applications or services configured to launch at startup
  Shortcuts in startup folders, Scheduled Tasks, or software installation processes affecting registry entries
  Error message at startup
    Disable program using MSconfig

## Slide 58
Figure 14-5 Error messages during Windows startup
and what to do about them (continues)

## Slide 59
Figure 14-5 Error messages during Windows startup
and what to do about them (continued)

## Slide 60: How to Recover Lost Data
Use Windows tools, third party software, or commercial data recovery services
Recovering a deleted or corrupted data file
  Look in the Recycle Bin
  Restore it from backup using the Backup and Restore window or use Previous Versions tab on file’s Properties box
  Use the Recover command
  Use application manufacturer’s web site
  Use third party software

## Slide 61: How to Recover Lost Data
Recover data from a computer that will not boot
  Remove hard drive and install as a second nonbooting hard drive in another system
  Use IDE to USB or a SATA to USB converter kit
    Temporarily connect hard drive to a USB port on a working computer
    Browse drive and copy data using Windows Explorer
Use a data recovery service
  Search for “data recovery” on the Internet
  Read up on reviews, understand warranty and guarantees, and get a recommendation

## Slide 62: Summary
When a system is turned on, startup BIOS takes control to examine hardware components and find an OS to load
Windows 7/Vista startup is managed by Windows Boot Manager(BootMgr) and Windows Boot Loader (WinLoad.exe)
Advanced Boot Options menu offers many options that are useful when troubleshooting startup problems

## Slide 63: Summary
Windows Recovery Environment (Windows RE) includes tools such as System Repair, Memory Diagnostics, System Restore, a command prompt window, and System Image Recovery
Windows tools and techniques used to troubleshoot a failed boot include Last Known Good Configuration, Startup Repair, System Restore, Safe Mode, Command Prompt, in-place upgrade of Windows, reimaging the hard drive, and reinstalling Windows

## Slide 64: Summary
In a failed Windows boot, it is important to determine at what point in the boot the failure occurred
If a hard drive will not boot, data recovery might be possible by installing the drive in another system as a second, nonbooting hard drive