## Slide 1: A+ Guide to Managing & Maintaining Your PC, 8th Edition
Chapter 19
Supporting Notebooks

## Slide 2: Objectives
Learn about special considerations when supporting notebooks that are different from supporting desktop computers
Learn how to configure, optimize and troubleshoot slots, ports, and peripheral devices used with notebooks
Learn how to replace and upgrade internal components in a notebook and all-in-one computer
Learn how to troubleshoot hardware problems with notebooks

## Slide 3: Special Considerations When Supporting Notebooks
Notebook (laptop): portable computer
  Varieties: tablet PCs and netbooks
    Tablet PC has more features than a notebook
    Netbook is smaller and has less features than notebook
Comparing notebooks to desktop computers
  Use the same technology as desktops
  Smaller, portable, and uses less power
  Replacement parts cost more than desktops
Notebooks offer a variety of ports and slots

## Slide 4
Figure 19-2 Ports and slots on a notebook computer

## Slide 5: Warranty Concerns
Always check to see if notebook is under warranty before servicing
Contacting technical support: information needed
  Notebook model and serial number
  Purchaser name, phone number, address
Service options
  On-site
  Ship to authorized service center
  Phone assistance or online chat

## Slide 6
Figure 19-4 The model and serial number stamped on the bottom of a notebook are used to identify the notebook to service desk personnel.

## Slide 7: Service Manuals and Other Sources of Information
Service manuals save time
  Enables safe notebook disassembly
Locating documentation – Service manual
  Manufacturer’s physical manual
  Manufacturer’s Web site
    Support or FAQ pages
  Third party websites
User manual
  Provides basic maintenance tasks

## Slide 8: Diagnostic Tools Provided By Manufacturers
To determine problem components use diagnostic software provided by manufacturer
  Sources:
    Manufacturer’s Web site
    CDs bundled with the notebook
    Hard drive or floppy disk
  Example: PC-Doctor
    Included with Lenovo, Fujitsu, and HP notebooks
    Can be purchased separately

## Slide 9: The OEM Operating System Build
Operating system preinstalled at the factory
  Original equipment manufacturer (OEM)
  OS Build
    Customized installation of the OS
  Proprietary drivers
  Customized diagnostic software
Use caution when upgrading to new OS

## Slide 10: The OEM Operating System Build
Recovery partition and recovery CDs
  Hard drive recovery partition can contain OS
    May be hidden
    Files protected from access
    See user manual for access
    Can also use Disk Management utility in Windows
  Recovery CDs came bundled with older notebooks
    Provided by manufacturer
    Drivers and application setup programs
    Today’s laptops provide a way to create recovery media before there is a problem

## Slide 11
Figure 19-8 This notebook hard drive has a recovery partition that can be used to recover the system.

## Slide 12: The OEM Operating System Build
Operating system upgrades
  Perform only if necessary
Tips:
  Upgrade using OS build from manufacturer
  Ensure supporting device drivers included
  Follow OEM’s specific instructions
Off-the-shelf OS advice:
  Verify system component compatibility
  Ensure device drivers available
  Flash BIOS before upgrade, if necessary

## Slide 13: Maintaining Notebooks and Notebook Components
General guidelines:
  Do not touch LCD panel with sharp objects
  Do not pick up or hold by the lid
  Use OEM recommended battery packs
  Do not tightly pack in a suitcase – use carrying case
  Do not move while hard drive is being accessed
  Do not put close to appliances generating strong magnetic field
  Do not connect to the Internet using a public network without setting the network location to Public

## Slide 14: Maintaining Notebooks and Notebook Components
General guidelines: (cont’d.)
  Use passwords with each Windows user account
  Keep notebook at room temperature
  Keep OS current
  Keep away from smoke, water, dust
  Do not power up and down unnecessarily
  Do not run it while it is in the case, resting on pillow or covered by a blanket
  Protect notebook against ESD
  Remove CD/DVD before traveling
  Take precautions if notebook gets wet

## Slide 15: Maintaining Notebooks and Notebook Components
Cleaning tips:
  Clean LCD panel with a soft dry cloth
  Use compressed air
    To clean keyboard, track ball, and touch pad
    To blow out air vents
    Remove keyboard if keys are sticking and then blow air under keys
  Use contact cleaner
    Battery connections

## Slide 16: Special Keys, Buttons, and Input Devices on a Notebook
Button or switches might be above the keyboard
  Most of the same settings that these buttons control may also be changed using Windows tools
Some settings might be:
  Volume
  Screen brightness
  Dual displays
  Bluetooth or Wi-Fi

## Slide 17
Figure 19-12 Control dual monitors on a laptop

## Slide 18: Special Keys, Buttons, and Input Devices on a Notebook
Common laptop pointing devices
  Touch pad, TrackPoint or point stick
  Some prefer USB wired or wireless mouse
Figure 19-13 The touch pad is the most common pointing device on a notebook

## Slide 19: Special Keys, Buttons, and Input Devices on a Notebook
Adjust touch pad or TrackPoint
  Mouse Properties box:
    Adjust pointer speed, mouse trails, pointer size, how the touch pad buttons work, other settings for pointing devices
Tablet PCs
  Stylus controlled from the Pen and Input Devices box
    Accessed from Windows Control Panel

## Slide 20: PCMCIA and ExpressCard Slots
Most peripheral devices today use a USB port to connect to a notebook
Older notebooks offered slots to connect peripherals
  Personal Computer Memory Card International Association (PCMCIA)
  Include variations of PC Card, CardBus, ExpressCard
PC Card slot technologies
  16-bit ISA bus
  Three standards pertaining to size and thickness
    Type 1, Type II, Type III

## Slide 21: PCMCIA and ExpressCard Slots
CardBus
  Increases bus width to 32 bits
  Backward compatible with earlier standards
ExpressCard matches PCI Express and USB 2.0
  Two sizes: ExpressCard/34 and ExpressCard/54
  Not backward compatible
  Hot-pluggable, hot-swappable, and supports autoconfiguration

## Slide 22
Figure 19-18 This notebook has one CardBus slot and one ExpressCard slot

## Slide 23: PCMCIA and ExpressCard Slots
Windows services for PC Card or ExpressCard
  Socket service and card service
Removing card from PC card or ExpressCard slot
  Use the Safely Remove Hardware icon in the notification area
  Proceed to eject the card

## Slide 24: Updating Port or Slot Drivers
If problems arise with a port or slot:
  Use Device Manager to see if errors are reported
Backups of drivers may be stored on hard drive
  Download the latest drivers from manufacturer’s web site
If problem is not solved by updating drivers:
  Use Device Manager to uninstall the port or slot drivers
  Then use support tools to reinstall the drivers

## Slide 25: Power and Electrical Devices
Notebook power sources
  AC adapter or a battery pack
Auto-switching AC adapter feature
  Device automatically switches from 110 V to 220 V AC power
Today’s batteries use:
  Lithium Ion Technology
Some notebooks use two batteries
  Second battery is known as a sheet battery

## Slide 26: Power and Electrical Devices
Notebook power needs
  A DC adapter for travel
    Inverter changes DC to AC
Figure 19-26 An inverter changes DC to AC and provides an outlet for your laptop’s AC adapter

## Slide 27: Power Management
Use power management settings to conserve power
Power-saving states
  Sleep mode: also called suspend mode
    Saves power when computer is not in use
  Hibernation: work is saved to hard drive and powers system down
Older computers allows power settings to be configured in Windows and in BIOS setup
  Newer BIOS does not control power settings that might conflict with Windows settings

## Slide 28: Power Management
Using the Advanced Configuration and Power Interface (ACPI) standards, BIOS might refer to 5 S states:
  S1: hard drive and monitor are turned off, everything else runs normally
  S2: processor is also turned off
  S3: everything is shut down except RAM and enough of the system to respond to a wake-up (sleep mode)
  S4: hibernation
  S5: power off state after a normal shutdown

## Slide 29: Port Replicators and Docking Stations
Port replicator
  Easy connection to full-sized monitor, keyboard, AC power adapter, and other devices
Docking station
  Same functions as port replicator
  Additional slots for adding secondary storage devices and expansion cards

## Slide 30: Replacing and Upgrading Internal Parts
Topics:
  Alternatives to consider before taking on complex repair projects
  How to upgrade memory
  How to exchange a drive
  How to perform other complex repair projects
    Exchanging an LCD panel or motherboard

## Slide 31: Three Approaches to Dealing with a Broken Internal Device
Factors to consider before starting repair project:
  Warranty
  Time the repair will take
  Alternatives to fixing (upgrading)
    Return notebook to manufacturer or service center
    Substitute external component for internal device
    Replace the internal device

## Slide 32: Three Approaches to Dealing with a Broken Internal Device
Before replacing or upgrading a component:
  Back up important data if possible
  Ground yourself against ESD
  Remove ExpressCards, CDs, DVDs, flash memory cards, or USB devices and then shut down notebook
  Disconnect AC adapter
  Undock (if necessary) and remove the battery

## Slide 33: Upgrading Memory
Memory used in notebooks
  SO-DIMMs (small outline DIMMs)
    DDR3 or DDR2
  SO-RIMMs (small outline RIMMs) – used by older notebooks
Can only use the type of memory the notebook is designed to support

## Slide 34
Table 11-2 Memory modules used in notebook computers

## Slide 35: Upgrading Memory
How to upgrade notebook memory:
  Upgrade process is similar to desktops
  Considerations:
    Make sure warranty not being voided
    Search for best buy on a suitable and authorized part
  General steps:
    Decide how much memory to upgrade
    Purchase memory
    Install it
  Follow steps outlined in the chapter

## Slide 36: Replacing a Hard Drive
General guidelines:
  See manufacturer’s documentation for drive sizes and connector types
  Be aware of voiding manufacturer’s warranty
Shopping:
  Notebook drive: 2.5 inches wide
    May use SSD (solid state device) technology
  Hard drives connector: SATA or PATA (IDE)
  44-pin IDE drive may use adapter to interface between proprietary connector and motherboard

## Slide 37: Replacing a Hard Drive
Issues to consider before replacing hard drive:
  Old drive crashed
    Recovery media and notebook drivers CD required
  Upgrade: must transfer data from old drive to new one
Older notebook computers required disassembly
Newer notebooks: easy to replace
  If BIOS setup uses autodetect:
    System boots up and BIOS recognizes new drive
    Searches for an operating system
    If a new drive: boot from Windows recovery CD

## Slide 38
Figure 19-41 Push the drive out of its bay
Figure 19-40 This one screw holds the hard drive in position

## Slide 39: Disassembling and Reassembling a Notebook Computer
Requires special tools and extra patience
Figure 19-43 To protect the system against ESD, attach the alligator clip of a ground strap to an I/O port on the back of the notebook.
Figure 19-44 Tools for disassembling a notebook computer.

## Slide 40: Disassembling and Reassembling a Notebook Computer
Many small screws require smaller tools
Work methodically:
  Keep screws and components organized
    Place screws in a pillbox (label each compartment)
    Place screws on soft padded work surface
      Use white labeling tape
    Place screws on notebook paper
      Write where screw belongs
    Tape screw beside manufacturer documentation
  Keep notes to help with reassembly

## Slide 41
Figure 19-46 Using a notepad can help you organize screws so you know which screw goes where when reassembling
Figure 19-47 Tape screws beside the step in the manufacturer documentation that told you to remove the screw.

## Slide 42: Disassembling and Reassembling a Notebook Computer
Disassembly tips:
  Find the hardware service manual
  Consider the warranty might still apply
    Opening the case might void the warranty
  Take the time necessary, do not force anything
  Protect against ESD
  Understand ZIF connectors
  Pry up plastic covers with dental pick or screwdriver
  Plastic screws may be used only once
  Disassemble components in order

## Slide 43: Disassembling and Reassembling a Notebook Computer
Reassembly tips:
  Reassemble notebook in reverse order
  Tighten, but do not over tighten, all screws
  Before installing the battery or AC adapter verify there are no loose parts inside the notebook

## Slide 44: Disassembling and Reassembling a Notebook Computer
Replacing the keyboard and touchpad:
  Power down and unplug notebook
  Remove screws on notebook bottom
  Open Lid
    Push keyboard toward lid while pulling it up to release it from the case
  Bring keyboard out of the case and forward
    Expose keyboard ribbon cable
    Use screwdriver to lift cable connector up and out
  Replace keyboard following steps in reverse order
  If touchpad is part of keyboard bezel, remove keyboard before removing the keyboard bezel

## Slide 45: Disassembling and Reassembling a Notebook Computer
Replacing optical drives:
  Remove keyboard
  Remove screw holding DVD drive to notebook
  Slide drive out of the bay and new drive into the bay
    Ensure connection with drive connector
    Replace the screw
Replacing expansion cards:
  Newer notebook use Mini PCI Express slots (Mini PCIe)
    Uses 52 pins on the edge connector
  Older notebooks use a Mini PCI slot

## Slide 46: Disassembling and Reassembling a Notebook Computer
Steps to remove a Mini PCIe wireless network card:
  Disconnect antenna from Wi-Fi card
  Remove the one screw at the top of the card
  Pull card forward and out of the slot
Figure 19-61 How to remove a Mini PCI Express card

## Slide 47: Disassembling and Reassembling a Notebook Computer
Replacing the processor:
  Use CPU supported by manufacturer and notebook model
  For many laptops, remove the cover on the bottom to expose the processor fan and heat sink assembly
  Some laptops may require you to remove the keyboard and keyboard bezel to reach the fan assembly and processor

## Slide 48
Figure 19-63 Remove the cover from the bottom of the laptop to expose
the heat sink and fan assembly and to reach the processor

## Slide 49: Disassembling and Reassembling a Notebook Computer
Replacing the motherboard:
  Need to fully disassemble the entire notebook
    Consider alternatives before proceeding
  General procedure for replacing the motherboard:
    Remove the keyboard, optical drive, and mini PCIe card
    Remove the notebook lid and keyboard bezel assembly
    Lift up the assembly and disconnect two cables connecting it to the motherboard
    Remove CPU and DVD drive
    Remove screw that hold motherboard in place

## Slide 50
Figure 19-71 Remove the single screw attaching the motherboard to the case

## Slide 51: Disassembling and Reassembling a Notebook Computer
Replacing the LCD panel:
  If LCD panel is dim or black:
    Connect external monitor to video port
  Toggle between LCD panel, external monitor, and both the panel and monitor
    If external monitor works: LCD panel assembly likely broken
    If LCD display entirely black: replace LCD assembly
    If LCD display dim: video inverter problem
  High-end notebooks contain video card
    May need to replace it too

## Slide 52: Disassembling and Reassembling a Notebook Computer
General directions to replace an LCD panel:
  Remove AC adapter and battery pack
  Remove the keyboard
  Remove screws holding hinge in place
    Remove hinge cover
  Remove screws holding LCD panel to the notebook
  Remove LCD panel from the notebook
  Remove screws holding the top cover and LCD panel
  Disconnect old inverter and install the new one
  Reattach LCD panel assembly to the notebook

## Slide 53: Working Inside An All-In-One Computer
All-in-one computer: uses a mix of components sized for a desktop and a notebook
  For some components, you’ll need to buy replacements from the manufacturer because they are most likely proprietary
  See the service manual for specific directions about replacing parts

## Slide 54
Figure 19-80 Components inside an all-in-one computer

## Slide 55: Troubleshooting Notebooks
Use diagnostics software to troubleshoot problems with notebook ports, slots or other devices
  Download from manufacturer’s web site if you don’t have it available on the hard drive
Next few slides cover some common problems with notebooks and how to solve them

## Slide 56: Problems Logging Onto Windows
Check to make sure NumLock is off
  Notebooks use this key to toggle between keys interpreted as letters and numbers
  Most notebooks have a NumLock indicator light near the keyboard

## Slide 57: No Wireless Connectivity
Notebook might have a switch to turn internal wireless adapter on and off
  Might also use a key combination for that purpose
  Ensure switch is set to on
For intermittent connectivity, ensure laptop is within range of wireless access point
Follow directions for your notebook to turn Bluetooth on

## Slide 58: Power or Battery Problems
If power is not getting to the system or battery indicator light is lit:
  Verify the AC adapter is plugged into an outlet
  Check if AC adapter’s plug is secure outlet
  Check connections on both sides of AC adapter transformer
  Check connection at notebook
If battery is not charging when AC adapter is plugged in, problem might be with battery or motherboard

## Slide 59: No Display
If LCD panel shows a black screen but power light is on:
  Look for an LCD cutoff switch or button on laptop
  Try to use the video port on the notebook to connect to an external monitor
  If external monitor does work, problem is with the LCD panel assembly
    Will need to replace inverter or LCD panel

## Slide 60: Flickering, Dim, or Otherwise Poor Video
Tips to solve problems with bad video:
  Verify Windows display settings
  Adjust the brightness
  Update the video drivers
  A flickering screen can be caused by bad video drivers, a low refresh rate, a bad inverter, or loose connections inside the laptop

## Slide 61: Summary
Notebook computers are designed for travel
The notebook manufacturer documentation are useful when disassembling, troubleshooting, and repairing a notebook
A notebook uses a customized installation of the Windows OS, customized by the manufacturer
A notebook hard drive is likely to contain a recovery partition or notebook may come with recovery CDs
PC Cards, CardBus, and ExpressCard slots are a popular way to add peripheral devices to notebooks

## Slide 62: Summary
Updating drivers for a port of slot can sometimes solve problems
A notebook can be powered by a battery pack or AC adapter connected to a power source
Windows 7/Vista uses sleep mode and hibernation to conserve power
When an internal component needs replacing, consider disabling the component and using an external peripheral device in its place
Current notebooks use SO-DIMMs for memory

## Slide 63: Summary
When upgrading components on a notebook, use components that are the same brand as notebook
Use diagnostics software from the notebook manufacturer to troubleshoot
Use a multimeter to check the voltage output of an AC adapter
Use an external monitor to verify that a video problem is with the LCD panel rather than internal video card or motherboard