## Slide 1: A+ Guide to Managing & Maintaining Your PC, 8th Edition
Chapter 2
Working Inside a Computer
Notes: 1

## Slide 2: Objectives
Learn how to take a computer apart and put it back together
Learn about the methods and devices for keeping a system cool
Learn how to select a power supply to meet the power needs of a system

## Slide 3: How to Work Inside a Computer Case
Every PC technician should know how to take a computer apart and put it back together again
The following slides will cover this skill

## Slide 4: Step 1: Plan and Organize Your Work
Make notes for backtracking
Remove loose jewelry that might get caught
Stay organized by keeping small parts in one place
Do not stack boards on top of each other
Do not touch board chips
  With hands, magnetized screwdriver
  Fingerprints on edge connectors may later cause corrosion

## Slide 5: Step 1: Plan and Organize Your Work
Protect yourself and the equipment
  Never ever touch inside of a turned on computer
  Consider monitor, power supply as “black boxes”
    Never remove the cover or touch inside
  Protect against static electricity
  Watch out for sharp edges that can cut

## Slide 6: Step 2: Open the Computer Case and Examine the System
Back up important data
Power down the system and unplug it
  Unplug other peripherals as well
Press and hold the power button for 3 seconds
  This will drain the power supply
Have a plastic bag or cup handy to hold screws
Open the case cover
  Many newer cases require you to remove the faceplate first
  Some older cases require you to remove a side panel

## Slide 7
Figure 2-2 Decide which side panel to remove

## Slide 8
Figure 2-3 Locate the screws that hold the side panel in place

## Slide 9
Figure 2-4 On this system, clips hold the side panel in place

## Slide 10
Figure 2-5 Slide the panel to the rear of the case

## Slide 11
Figure 2-6 Newer cases require you to remove the front panel
before removing the side panel of a computer case

## Slide 12
Figure 2-7 One screw holds the side panel in place

## Slide 13
Figure 2-8 Slide the side panel to the front of the case
and then lift it off the case

## Slide 14: Step 2: Open the Computer Case and Examine the System
Clip your ground bracelet to the side of the computer case
After opening you will see the main components:
  Power supply
  Motherboard
  Drives
Trace cables from motherboard to the component to know the purpose of each cable

## Slide 15
Figure 2-9 Attach the alligator clip of your ground bracelet
to the side of the computer case

## Slide 16: Step 3: Remove Expansion Cards
If removing components:
  Draw a diagram of all cable connections to the motherboard, expansion cards, and drives
  Use a felt-tip marker to mark components in order to indicate a cable connection, board placement, orientation, etc..

## Slide 17
Figure 2-10 Diagram the pin locations of the color-coded
wires that connect to the front of the case

## Slide 18: Step 3: Remove Expansion Cards
To remove expansion cards:
  Remove any wire or cable connected to the card
  Remove the screw holding the card to the case
  Grasp the card with both hands and remove it by lifting straight up (can also rock the card from end to end)
  Don’t put your fingers on edge connectors or touch a chip
    It is best to store cards in an antistatic bag

## Slide 19: Step 4: Remove the Motherboard, Power Supply, and Drives
Depending on the system, you may have to remove the drives and/or power supply to get to the motherboard
To remove motherboard:
  Unplug power supply lines
  Unplug PATA, SATA, and floppy drive cables
  Disconnect wires leading from the front of the computer case to the motherboard (called front panel connectors)
    Make a diagram before disconnecting

## Slide 20: Step 4: Remove the Motherboard, Power Supply, and Drives
To remove motherboard (cont’d):
  Disconnect any other cables or wires connected to the motherboard
  Unscrew motherboard from spacers
    Spacers (standoffs): round plastic or metal pegs that separate the board from the case
    Spacers are necessary to keep motherboard from touching the metal case, which might cause a short
  Motherboard should be free to remove from the case

## Slide 21
Figure 2-16 Remove the motherboard from the case

## Slide 22: Step 4: Remove the Motherboard, Power Supply, and Drives
To remove the power supply from the case:
  Look for screws that attach the power supply to the computer case
    Do not remove screws that hold power supply housing together (do take housing apart)
  Sometimes power supplies are also attached to the case on the underside by recessed slots
    Turn case over and look for slots
    If present, determine in which direction you need to slide the power supply to free it from the case

## Slide 23
Figure 2-17 Removing the power supply mounting screws

## Slide 24: Step 4: Remove the Motherboard, Power Supply, and Drives
Tips to remove drives:
  Look for screws on each side of the drive attaching the drive to the drive bay
  There might be a catch underneath the drive
    You must lift up as you slide the drive forward
  Some drive bays have a clipping mechanism to hold the drive in the bay
    Release the clip and then pull the drive forward
  May have to remove the drive bay in order to remove the drives

## Slide 25
Figure 2-18 To remove this CD drive, first pull the clip forward to
release the drive from the bay

## Slide 26
Figure 2-19 Push down on the clip and then slide the removable
bay forward and out of the case

## Slide 27
Figure 2-20 Drives in this removable bay are held in place
with screws on each side of the bay

## Slide 28: Steps to Put a Computer Back Together
Refer to any diagrams created during the disassembling process
Install components in this order: power supply, drives, motherboard, and cards
  When installing drives, it may be easier to connect cables to the drives before sliding them into the bay
Place motherboard inside the case
  Make sure ports and screw holes are lined up

## Slide 29
Figure 2-22 Align screw holes in the case with those on the motherboard

## Slide 30: Steps to Put a Computer Back Together
Connect the power cords from the power supply to the motherboard
  Will always need the main P1 power connector and may likely need the 4-pin auxiliary connector for the processor
  A board might have a 6-pin or 8-pin PCIe power connector
    If power supply does not have this connector, use an adapter to convert two Molex connectors to a PCIe connector

## Slide 31
Figure 2-24 The 24-pin connector supplies power to the motherboard

## Slide 32
Figure 2-25 The auxiliary 4-pin power cord provides power to the processor

## Slide 33: Steps to Put a Computer Back Together
Connect the power cords from the power supply to the motherboard (cont’d):
  If case fan is present, connect power cord from the fan to pins on motherboard labeled “Fan Header”
  If a CPU and cooler are already installed on motherboard, connect power cord from CPU to pins on motherboard labeled “Fan Header”
Connect wire leads from the front panel of the case to the front panel header on motherboard

## Slide 34
Figure 2-28 Seven connectors from the front panel connect to the motherboard

## Slide 35
Figure 2-29 Front panel header uses color-coded pins and labels

## Slide 36: Steps to Put a Computer Back Together
Look for a small triangle embedded on the connector that marks one of the outside wires as pin 1
  Line up pin 1 on connector with pin 1 marked on motherboard
  If labels on motherboard are not clear, consult user guide for help
Figure 2-30 Look for the small triangle embedded
on the wire lead connectors to orient the connector
correctly to the motherboard connector pins

## Slide 37: Steps to Put a Computer Back Together
Connect wires to ports on the front panel of the case
  Audio ports or USB ports are examples
Install the video card and other expansion cards
Double-check each connection
Plug in keyboard, monitor, and mouse
In classroom environment, have instructor check work
Turn on the power and check that the PC is working properly
  If not, most likely a loose connection

## Slide 38: Cooling Methods and Devices
If processor, expansion cards, and other components overheat:
  System can get unstable
  Components can fail or be damaged
Devices used to cool a system:
  CPU and case fans
  Coolers
  Heat sinks
  Liquid cooling systems
  Dust-preventing tools

## Slide 39: Processor Coolers, Fans, and Heat Sinks
Intel maximum heat limit:
  185 degrees F/85 degrees C
Good processor coolers maintain a temperature of:
  90-110 degrees F (32-43 degrees C)
Cooler: sits on top of processor
  Consists of a fan and heat sink
  Heat sink: uses fins that draw heat away from processor
  Fan: blows drawn heat away from CPU unit

## Slide 40
Figure 2-35 A cooler sits on top of a processor to help keep it cool

## Slide 41: Processor Coolers, Fans, and Heat Sinks
Cooler (cont’d):
  Made of aluminum, copper or combination of both
  Bracketed to motherboard using a wire or plastic clip
  A creamlike thermal compound eliminates air pockets, helping to draw heat off the processor
    Found between bottom of cooler heatsink and top of processor
    Makes an airtight connection between fan and processor
  Gets power using a 4-pin fan header on the motherboard

## Slide 42
Figure 2-37 Thermal compound is already stuck to the bottom of this
cooler that was purchased boxed with the processor

## Slide 43
Figure 2-38 A cooler fan gets its power from a 4-pin PWM
header on the motherboard

## Slide 44: Case Fans and Other Fans and Heat Sinks
Case fans: help draw air out of the case to prevent overheating
  Most cases have one or more positions on the case to hold a case fan
  Large fans tend to perform better than small fans
Other fans:
  Some graphics (video) cards come with a fan
  Fan cards can be mounted next to graphics cards
    Be sure to select a fan card that fits the expansion slot you plan to use

## Slide 45
Figure 2-40 A PCI fan card by Vantec can be used next to a
high-end graphics card to help keep it cool

## Slide 46: Case Fans and Other Fans and Heat Sinks
Other fans (cont’d):
  RAM cooler – clips over a DIMM memory module
    May be powered by a SATA or 4-pin Molex power connector
Figure 2-41 A RAM cooler keeps memory modules cool

## Slide 47: Liquid Cooling Systems
Liquid cooling system
  A small pump sits inside the case and tubes moves liquid around components and then away from them to a place where fans cool the liquid
Figure 2-42 A liquid cooling system pumps
liquid outside and away from components
where fans can then cool the liquid

## Slide 48: Dealing With Dust
Dust:
  Insulates PC parts like a blanket causing overheating
  Can jam fans which may also cause overheating
Dust can be blown out of the case using a can of compressed air or by using a antistatic vacuum
  Should be part of a regular preventative maintenance program (at least twice a year)
  Good idea to blow or vacuum keyboard as well

## Slide 49: Selecting a Power Supply
Reasons to purchase a power supply:
  Building a new system from scratch
  Power supply in existing system fails
  Power supply in existing system is not adequate
When building from scratch, some cases come with power supply already installed

## Slide 50: Types and Characteristics of Power Supplies
Important power supply feature considerations:
  Form factor determines power supply size
  Wattage ratings (listed in documentation)
  Type and number of power cables, and connectors
  Fans inside the PSU
  Warranty and overall quality

## Slide 51: How to Calculate Wattage Capacity
Determining wattage capacity
  Consider all components inside case
  Consider USB and FireWire devices
    Get power from ports connected motherboard
Points to keep in mind
  Video cards draw the most power
  Use power supply rated 30 percent higher than expected
What size Power Supply?
  Add up wattage requirements and add 30 percent

## Slide 52
Table 2-1 To calculate power supply rating, add up total wattage

## Slide 53: Summary
When working inside a computer, stay organized, keep careful notes, and follow all safety procedures
Before opening a case, shut down the system, unplug it, disconnect all cables, and press the power button to drain residual power
An expansion card fits in a slot on the motherboard and is anchored to the case by a single screw or clip
Devices used to keep a processor and system cool include CPU coolers, fans, heat sinks, and liquid cooling

## Slide 54: Summary
Liquid cooling system use liquids pumped through system to keep it cool
Important features of a power supply to consider when purchasing it are: form factor, wattage capacity, number and type of connectors, fan size, support dual video cards, and warranty
To decide on the wattage capacity of a power supply, add up the wattage requirements for all components and add 30 percent