## Slide 1: A+ Guide to Managing & Maintaining Your PC, 8th Edition
Chapter 4
All About Motherboards
Notes: 1

## Slide 2: Objectives
Learn about the different types and features of motherboards
Learn how to use setup BIOS and physical jumpers to configure a motherboard
Learn how to maintain a motherboard
Learn how to select, install, and replace a motherboard

## Slide 3: Motherboard Types and Features
Motherboard
  Most complicated computer component
  One of the first items to consider when building a computer
Consider the following when purchasing a motherboard:
  Form factor
  Processor socket and chipset
  Buses and number of bus slots
  Other connectors, slots, and ports

## Slide 4: Motherboard Form Factors
Determines motherboard size, features
  Compatible with power supplies, cases, processors, expansion cards
Most popular
  ATX, MicroATX, and Mini-ITX
    Mini-ITX is smaller than MicroATX and is also known as ITX
The following slides show examples of form factors and comparisons of sizes and hold positions of several form factors

## Slide 5
Figure 4-3 A Mini-ITX motherboard

## Slide 6
Table 3-1 Sockets for Intel processors used for desktop computers

## Slide 7: Processor Sockets
Processor socket – determines which processors a board can support
  Socket holds Intel or AMD processor
Sockets for Intel processors
  Intel makes several Itanium and Xeon processors designed for servers

## Slide 8: Processor Sockets
Sockets and processor use different methods to make contacts between them:
  Pin grid array (PGA) socket
    Pins aligned in uniform rows around socket
  Land grid array (LGA)
    Uses lands (pads) rather than pins
    Examples of LGA sockets: LGA775 and LGA1366
  Flip-chip land grid array (FCLGA) socket
    Chip is flipped over so that the top of the chip is on the bottom and makes contact with the socket

## Slide 9: Processor Sockets
Sockets and processor use different methods to make contacts between them (cont’d):
  Staggered pin grid array (SPGA)
    Pins staggered over socket
    Squeezes more pins into a small space
    Easily bent
  Ball grid array (BGA)
    Not really a socket
    Processor is soldered to the motherboard

## Slide 10
Figure 4-6 Socket LGA775 is the first Intel socket to use lands rather than pins

## Slide 11: Processor Sockets
Zero insertion force (ZIF) sockets
  All current processor sockets
  Side lever lifts processor up and out of the socket
Sockets for AMD Processors
  AMD uses the PGA socket architecture (desktops)

## Slide 12
Table 3-3 Sockets for AMD processors used for desktop computers

## Slide 13: Processor Sockets
Match a processor to the socket and motherboard
  Refer to motherboard, processor compatibility documentation
Figure 4-9 AMD Athlon 64 processor to be inserted into an AM2+ socket

## Slide 14: The Chipset
Chipset: set of chips on motherboard that work with processor to collectively control:
  Memory, motherboard buses, some peripherals
Manufacturers
  Intel, AMD, NVIDIA, SiS, and VIA
Intel Chipsets
  North Bridge and South Bridge - Uses hub interface
    All I/O buses (input/output buses) connect to hub
      Hub connects to system bus
    North Bridge – fast end of hub
    South Bridge – slow end of hub

## Slide 15
Figure 4-10 The chipset’s North Bridge and South Bridge control access to the
processor for all components

## Slide 16: The Chipset
Intel Chipsets (cont’d)
  Core i7 and X58 chipset
    Referred to by Intel as Nehalem chipset
    Contain memory controller within processor housing
    Memory connects directly to processor
    Has QuickPath Interconnect (QPI) technology
      Has 16 lanes for data packets
  Sandy Bridge chipset
    Memory and graphics controller in processor
    Second Generation Core i7 processor is an example
    Sandy Bridge motherboards use DDR3 memory

## Slide 17
Figure 4-11 X58 chipset architecture

## Slide 18: The Chipset
Intel Chipsets (cont’d)
  Ivy Bridge chipset – 3rd generation processors released in 2012
    Use less power
    More transistors in a smaller place
    Perform better than earlier products
    Uses a single Platform Controller Hub

## Slide 19: The Chipset
AMD chipsets
  AMD A-series (code name Trinity)
    Designed to compete with Ivey Bridge chipsets
  AMD 9-series, 8-series, and 7-series
    Designed for gamer, hobbyist, multimedia enthusiast
    Focus on good graphics capabilities
    Support overclocking
  AMD 580X Crossfire chipset
    Supports ATI CrossFire
  AMD 780V chipset
    Designed for business needs
  AMD 740G and 690 chipsets
    Designed for low-end, inexpensive systems

## Slide 20: The Chipset
NVIDIA, SIS and VIA Chipsets
  All make graphics processors and chipset for AMD and Intel processors
  NVIDIA’s method of connecting multiple video cards is called SLI
  If planning a gaming computer using two video cards:
    Look for a motherboard that supports SLI and uses the nForce chipset

## Slide 21: Buses and Expansion Slots
Bus
  System of pathways used for communication
Carried by bus:
  Power, control signals, memory addresses, data
Data and instructions exist in binary
  Only two states: on and off
Data path size: width of a data bus
  Examples: 8-bit bus has eight wire (lines) to transmit

## Slide 22
Figure 4-16 A data bus has traces or lines that carry voltage interpreted
by the CPU and other devices as bits

## Slide 23: Buses and Expansion Slots
System clock (system timer) – times activities on the motherboard
Speed of memory, Front Side Bus, processor, or other component is measured in hertz (Hz), which is one cycle per second
  Megahertz (MHz): one million cycles per second
  Gigahertz (GHz): one billion cycles per second
Motherboards can have more than one bus
  Table 3-4 on the following slide lists many buses

## Slide 24
Table 3-4 Buses listed by throughput

## Slide 25: Buses and Expansion Slots
Conventional PCI
  Improved several times
  Four types of slots and six possible PCI card configurations

## Slide 26: Buses and Expansion Slots
PCI-X
  Uses 64-bit data path
  Latest revision is PCI-X 3.0 (all revisions are backward-compatible)
Figure 4-19 The two long white
PCI-X slots can support PCI cards

## Slide 27: Buses and Expansion Slots
PCI Express (PCIe)
  Not backward compatible with conventional PCI or PCI-X
  Expected to replace both PCI and PCI-X in the future
  Uses a serial bus, which is faster than parallel
  Comes in four different slot sizes
    PCI Express x1, x4, x8, and x16
  Latest version is PCIe 3.0 which doubles the throughput of version 2.0

## Slide 28
Figure 4-21 Three types of PCIe slots and one conventional PCI slot

## Slide 29: Buses and Expansion Slots
PCI Riser cards
  Installs in a PCI slot and provides another slot at a right angle
  Used to fit PCI, PCIe, and PCI-X cards into a low-profile or slimline case
Figure 4-23 PCI riser card provides a 3.3-V slot or 5-V slot depending on which direction the card is inserted in the PCI slot

## Slide 30: Buses and Expansion Slots
AGP Buses
  Accelerated Graphics Port (AGP) – standard used by motherboard video slots and video cards for years
  Will need to know how to support it even though it is a dying technology
  AGP standards include:
    Three major releases - AGP 1.0, AGP 2.0, AGP 3.0
    One major change in slot length – AGP Pro
    Four different speeds – 1x, 2x, 4x, and 8x
    Three different voltages
    Six different slots

## Slide 31
Table 3-5 AGP standards summarized

## Slide 32: On-Board Ports and Connectors
On-board ports (integrated components)
  Ports coming directly off the motherboard
    USB, sound, network, video, eSATA ports
    Older motherboards might have mouse and keyboard ports, parallel and serial ports
I/O shield
  Plate installed in computer case providing holes for on-board ports
Internal connectors
  Parallel ATA, floppy drive, serial ATA, SCSI, USB or FireWire (IEEE 1394) connectors

## Slide 33: Configuring a Motherboard
Motherboard settings
  Enable or disable connector or port
  Set CPU frequency, system bus, other buses
  Control security features
  Control what happens when PC first boots
Three ways to configure older motherboards:
  DIP switches, jumpers, CMOS RAM
Today, almost all motherboard configuration data is stored in CMOS RAM
  Program called BIOS setup or CMOS setup is used to make changes to settings stored in CMOS RAM

## Slide 34: Using Jumpers to Configure a Motherboard
Jumper – two small posts or metal pins that stick up off the motherboard that is open or closed
  Open jumper has no cover and a closed jumper has a cover on the two pins
  Retain setup or installation information
  Jumpers can be used to clear a forgotten supervisor or power-on password

## Slide 35
Figure 4-35 This group of three jumpers controls the BIOS configuration
Figure 4-36 BIOS configuration jumper settings

## Slide 36: Using Setup BIOS To Configure a Motherboard
Access the BIOS Setup Program
  Press a key or combination of keys during the boot process
    Varies from one manufacturer to another
    See documentation for your motherboard or watch the screen near the beginning of the boot
  Setup screen appears with menus and Help features

## Slide 37
Figure 4-37 BIOS setup main menu

## Slide 38: Using Setup BIOS To Configure a Motherboard
Change the boot sequence
  Might need to change boot sequence from hard drive to DVD
  Unified Extensible Firmware Interface (UEFI) – new standard slowly replacing BIOS
    Interface between firmware on motherboard and the OS
    Improves the boot process
    UEFI is new boot option

## Slide 39: Using Setup BIOS To Configure a Motherboard
Configure onboard devices
  Enable/disable a port or group of ports
View hard drive and optical drive information
Processor and clock speeds
  Some motherboards allow changing the processor speed and/or the memory multiplier
Monitor temperatures, fan speeds, and voltages
Intrusion detection
  Can enable event logging (logs when case is opened)

## Slide 40: Using Setup BIOS To Configure a Motherboard
Power-on passwords
  Assigned in BIOS setup to prevent unauthorized access to the computer and/or BIOS setup utility
  May be possible to set a supervisor and user password
    If both passwords are set, must enter a valid password to boot the system
  How to set passwords varies depending on motherboard and BIOS
    Some allow a System power-on password, which will require a password be entered every boot
    A Setup power-on password only requires a password be entered in order to access BIOS setup

## Slide 41: Using Setup BIOS To Configure a Motherboard
LoJack
  Technology embedded in the BIOS of many laptops to protect a system against theft
  Must subscribe to service
  Software and BIOS work together to locate a laptop whenever it connects to the Internet
Drive Encryption and Drive Password Protection
  Some motherboards allow you to set a password in order to access the hard drive
  Password kept on drive so that it still works even if drive is moved to another computer

## Slide 42: Using Setup BIOS To Configure a Motherboard
TPM chip – Trusted Platform Module chip
  BitLocker Encryption in Windows 7/Vista works with this chip
  Encryption key is kept on chip
  Assures that a drive cannot be used in another computer
Virtualization – when one physical machine hosts multiple activities that are normally on multiple machines
  Virtualization must be enabled in BIOS setup for VM software to work

## Slide 43: Using Setup BIOS To Configure a Motherboard
Exiting the BIOS setup menus
  Most exit screens give several options
Figure 4-50 BIOS setup Exit menu

## Slide 44: Maintaining a Motherboard
Motherboard is considered a field replaceable unit
  Need to know how to:
    Update motherboard drivers
    Update flash BIOS
    Replace CMOS battery

## Slide 45: Maintaining a Motherboard
Update motherboard drivers
  Device drivers are small programs that allow software to interact with certain hardware
  Use Windows internal drivers, bundled CD drivers, or download drivers from manufacturer site
Flash BIOS
  Process of upgrading or refreshing the ROM BIOS chip
  BIOS updates are downloaded from motherboard manufacturer’s Web site or third party site
  Performed if motherboard unstable, incorporating new feature, or component

## Slide 46: Maintaining a Motherboard
Methods of installing BIOS updates
  Express BIOS update
  Update from a USB flash drive using setup BIOS
  Update using a bootable CD
  Recovery from a failed update
“If it’s not broke, don’t fix it” – only update if you’re having trouble with a motherboard
Don’t update unless the update is a later version than the one installed
Update should not be interrupted while in progress

## Slide 47: Maintaining a Motherboard
Replacing the CMOS battery
  Choose correct replacement battery
  Power down system, unplug it, press power button to drain the power, remove case cover
  Use ground bracelet, remove old battery using a flat-head screwdriver, pop new battery into place

## Slide 48: Installing or Replacing a Motherboard
Consider the following when selecting a motherboard:
  Form factor
  The brand (Intel or AMD) and model processors the board supports
  Chipset and memory speeds the board supports
  Expansion slots (type and how many needed)
  Hard drive controllers
  Case
  Price and warranty
  Support

## Slide 49: Installing or Replacing a Motherboard
General process for replacing a motherboard:
  1. Verify right motherboard is selected
  2. Get familiar with documentation, features, settings
  3. Remove components to reach old motherboard
  4. Set any jumpers on the new motherboard
  5. Install the I/O shield (metal plate)
  6. Install motherboard
  7. Install processor and processor cooler
  8. Install RAM
  9. Attach cabling (case switches, power supply, drives)

## Slide 50: Installing or Replacing a Motherboard
General process for replacing motherboard (cont’d.)
  10. Install video card on motherboard
  11. Plug in PC, attach monitor, keyboard
  12. Boot system, enter BIOS setup
  12. Verify settings set to default
    Check time and date
    Make sure abbreviated POST is disabled
    Set the boot order
    Leave everything else at defaults
    Save and exit

## Slide 51: Installing or Replacing a Motherboard
General process for replacing motherboard (cont’d.)
  13. Observe POST, verify no errors
  14. Verify Windows starts with no errors
  15. Install the motherboard drivers
  16. Install other expansion cards and drivers
  17. Verify system operating properly, make final OS and BIOS adjustments (setting power-on passwords)

## Slide 52: Summary
The motherboard is the most complicated of all components inside a computer
Most popular motherboard form factors are ATX, MicroATX and Mini-ITX
Motherboard will have one or more processor sockets
Intel, AMD, NVIDIA, and SiS are the most popular chipset manufacturers
Major advancements in Intel: Accelerated Hub Architecture, Nehalem chipsets, Sandy Bridge and Ivy Bridge chipsets

## Slide 53: Summary
Buses include conventional PCI, PIC-X, PCI Express, and AGP
Some components can be built into the motherboard, called on-board components
Most common method of configuring a motherboard is BIOS setup
Settings that can be changed include: changing boot order, enabling or disabling onboard devices, support for virtualization, and security settings

## Slide 54: Summary
Motherboard drivers and/or BIOS might need updating to fix a problem
CMOS battery might need replacing
When selecting a motherboard pay attention to the form factor, chipset, expansion slots, memory slots, and processors supported
Study motherboard manual before installing it